## Slide 1: Computer Organization & Design 实验与课程设计
施青松
Asso. Prof. Shi Qingsong
College of Computer Science and Technology, Zhejiang University
zjsqs@zju.edu.cn
Computer Organization & Design
实验十二
多周期CPU指令扩展设计

## Slide 2: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 3: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 4: Task
1. Extend the instruction set for multicycle CPU
  To include at least the following instructions
    R-Type：add, sub, and, or, xor, nor, slt, srl*, jr, jalr, eret；
    I-Type： addi, andi, ori, xori, lui, lw, sw, beq, bne, slti
    J-Type： J, Jal*；
  Encourage to do customized design
    Must compatible with the basic instruction set
2. Design instruction set testing schema and program
  Testing schema and program
  Demo program: simple but meaningful
    Simplified version of project

## Slide 5: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 6: CPU organization
Digital circuit
  General circuits that controls logical event with logical gates --Hardware
Computer organization
  Special circuits that processes logical action with instructions -Software
Control unit
Datapath
Control signals
Status signals
Control output
Data input
Data output
Status input

## Slide 7: Multicycle datapath：compatible with 9-23+ instructions
Find datapath for each instruction：5+1个MUX
  Which part are added or modified？
修改

## Slide 8: Datapath of lab10：M_datapath
Key signals
  Branch
    Branch：=1→beq；=0 → bne
    Condition indication：PCWriteCond
  Path control signal
    MemtoReg(1:0)：4-to-1, lab10 use only 2 channels
    RegDst(1:0)：4-to-1, lab10 only use 2 channels
    PCSource(1:0)：4-to-1, lab10 only use 3 channels
  Other signals
    Inst_R：指令寄存器输出
    PC_Current：当前PC(PC+4)
    M_addr：存储器地址

## Slide 9: Datapath interface- M_datapath.v
module M_datapath(input clk,
input reset,
input MIO_ready, //外部输入=1
input IorD,
input IRWrite,
input[1:0] RegDst, //预留到2位
input RegWrite,
input[1:0]MemtoReg, //预留到2位
input ALUSrcA,
input[1:0]ALUSrcB,
input[1:0]PCSource, //4选1控制
input PCWrite,
input PCWriteCond,
input Branch,
input[2:0]ALU_operation,
output[31:0]PC_Current,
input[31:0]data2CPU,
output[31:0]Inst,
output[31:0]data_out,
output[31:0]M_addr,
output zero,
output overflow
);
endmodule

## Slide 10: Control signals：
兼容实验十基本多周期通路与操作控制
信号 | 源数目 | 功能定义 | 赋值0时动作 | 赋值1时动作
ALUScrA | ？ | ALU端口A输入选择 |  | 
ALUSrc_B(1:0) | ？ | ALU端口B输入选择 |  | 
RegDst(1:0) | ？ | 寄存器写地址选择 |  | 
MemtoReg(1:0) | ？ | 寄存器写入数据选择 |  | 
IorD | ？ | 指令或数据地址选择 |  | 
PCSource | ？ | Next-PC指针选择 |  | 
PCWriteCond | ？ | 条件指令指示 |  | 
Branch | ？ | Beq、Bne指示 |  | 
RegWrite | - | 寄存器写控制 |  | 
MemWrite | - | 存储器写控制 |  | 
MemRead | - | 存储器读控制 |  | 
…… | ？ | 个性化设计新增(需修改电路符号sym) |  | 
ALU_Control | 000- 111 | 3位ALU操作控制 | 参考表 Exp04 | Exp04
请填写信号赋值时
对应操作

## Slide 11: Controller and control object

## Slide 12: FSM for 18+instructions： asking the students to complete the corresponding state truth table
根据数据通路设计所有指令状态机

## Slide 13: Fill in the following table: refer to lab 11
状态 输出信号 | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001 | 增加 |  |  | 
 | IF | ID | MEN-Ex | MEN-RD | LW_WB | MEM_W | R_Exc | R_WB | Beq_Exc | J | …… | …… | …… | 
PCWrite |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PCWriteCond |  |  |  |  |  |  |  |  |  |  |  |  |  | 
IorD |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MemRead |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MemWrite |  |  |  |  |  |  |  |  |  |  |  |  |  | 
IRWrite |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MemtoReg1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MemtoReg0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PCSource1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PCSource0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ALUSrcA |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ALUSrcB1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ALUSrcB0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RegWrite |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RegDst1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RegDst0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Branch |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ALU_operation |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MEM_IO |  |  |  |  |  |  |  |  |  |  |  |  |  | 
…… |  |  |  |  |  |  |  |  |  |  |  |  |  | 
请分析完成输出信号真值表

## Slide 14: State table for 9 instructions as reference
建议直接输出ALU控制信号：ALU_operation
建议直接输出存储器写控制信号：men_w

## Slide 15: Controller implementation
Controller implementation
  Instruction implementation use one level decoding
    Main controller directly output ALU_operation
    ALU decoder can use the module of single cycle CPU
FSM implementation
  Suggest to use HDL description based on state table：
    Same as project design，easy for optimization and extension
    Separate output from state transition
      Clear struture
      HDL description
  note：there is one clock difference if put output and state machine together

## Slide 16: Controller module：ctrl
Key signals:
  Branch
    Branch：=1→beq；=0 → bne
    Condition indication：PCWriteCond
  Path control signal
    MemtoReg(1:0)：4-to-1, lab10 use only 2 channels
    RegDst(1:0)：4-to-1, lab10 only use 2 channels
    PCSource(1:0)：4-to-1, lab10 only use 3 channels
  Other signals
    MIO_ready：外设就绪
      =0 CPU等待；=1 CPU正常运行
      本实验恒等于1
    CPU_MIO：CPU访问存储器指示
    Inst_R：指令寄存器输出
    PC_Current：当前PC(PC+4)
    M_addr：存储器地址
    State_out：状态编码，用于测试

## Slide 17: Controller interface- ctrl.v
module ctrl(input clk,
input reset,
input [31:0] Inst_in,
input zero,
input overflow,
input MIO_ready, //外部输入=1
output reg MemRead,
output reg MemWrite,
output reg[2:0]ALU_operation, //ALU_Control
output [4:0]state_out,
output reg CPU_MIO,
output reg IorD,
output reg IRWrite,
output reg [1:0]RegDst, //实验十预留到2位
output reg RegWrite,
output reg [1:0]MemtoReg, //实验十预留到2位
output reg ALUSrcA,
output reg [1:0]ALUSrcB,
output reg [1:0]PCSource,
output reg PCWrite,
output reg PCWriteCond,
output reg Branch
);
endmodule

## Slide 18: U3-memory initialization：mem.coe code and data are together
memory_initialization_radix=16;
memory_initialization_vector=
3c03f000, 2014003f, 3c088000, 00632020, 20020001, 00000827, 00205020, 20070003, 00e73827, 20067fff,
00008820, 200502ab, ac650000, 20120002, ac600004, 8c650000, 00a52820, 00a52820, ac650000, ac660004,
3c0dffff, 8c650000, 00a52820, 00a52820, ac650000, 8c650000, 00a85824, 21ad0001, 11680015, 8c650000,
20120018, 00b25824, 11600005, 1172000a, 20120008, 1172000b, ac890000, 08000015, 11410001, 0800002a,
00005027, 014a5020, ac8a0000, 08000015, 8e2902a0, ac890000, 08000015, 8e290260, ac890000, 08000015,
3c0dffff, 014a5020, 01425025, 22310004, 02348824, 21290001, 11210001, 0800003b, 21290005, 8c650000,
00a55820, 016b5820, ac6b0000, ac660004, 8c650000, 00a85824, 1168fffd, 0800001d, 00000000, 00000000,
00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000,
………………
………………
f0000000, 000002AB, 80000000, 0000003F, 00000001, FFFF0000, 0000FFFF, 80000000, 00000000, 11111111, 22222222, 33333333, 44444444, 55555555, 66666666, 77777777, 88888888, 99999999, aaaaaaaa, bbbbbbbb, cccccccc, dddddddd, eeeeeeee, ffffffff, 557EF7E0, D7BDFBD9, D7DBFDB9, DFCFFCFB, DFCFBFFF, F7F3DFFF, FFFFDF3D, FFFF9DB9, FFFFBCFB, DFCFFCFB, DFCFBFFF, D7DB9FFF, D7DBFDB9, D7BDFBD9, FFFF07E0, 007E0FFF,
03bdf020, 03def820, 08002300;
Code section：address starts from 00000000
Data section：starting address needs to be appointed

## Slide 19: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 20: project：OExp12-MSOC
Extend the instruction set for multicycle CPU
  To include at least the following instructions
    R-Type：add, sub, and, or, xor, nor, slt, srl*, jr, jalr, eret；
    I-Type： addi, andi, ori, xori, lui, lw, sw, beq, bne, slti
    J-Type： J, Jal*；
Integration and substitution with verified new CPU
  Replace ctrl module of Exp11
  Replace M_Datapath of Exp11
  Top module is the same as Exp11
    name：OExp11_MCPU/MSOC.sch
Test extended CPU
  Design test program (MIPS assembling) to test

## Slide 21
Multicycle CPU extension
Datapath and controller design

## Slide 22: Design gist
Design extended datapath for multicycle CPU
  Modify datapath based on Exp11
  Implement datapath and simulation
Design extended controller for multicycle CPU
  Design state diagram based on new datapath and instruction execution
  Get state table and output truthtable based on state diagram
  Implement controller based on state table
    HDL structural description
  Controller simulation
Integration and substitution
  Replace ctrl.v of Exp11
  Still use top module of Exp11：name：OExp11_MCPU.v
Controller test
  Design test program (MIPS assembling) ：
  OP decoding test：R-format、memory access instr、branch instr，jump instr

## Slide 23: Extended M_Datapath design reference

## Slide 24: State table of 23 instructions for reference
首先完成状态真值表，然后设计状态机
由于信号定义和指令状态机划分不同结果也会不同

## Slide 25: Controller HDL description structure
Main controller state machine description
parameter IF = 5'b00000, ID=5'b00001, EX_R= 5'b00010, EX_Mem=5'b00011, EX_I= 5'b00100,
Lui_WB=5'b00101, EX_beq=5'b00110, EX_bne= 5'b00111, EX_jr= 5'b01000, EX_JAL=5'b01001,
Exe_J = 5'b01010, MEM_RD=5'b01011, MEM_WD= 5'b01100, WB_R= 5'b01101, WB_I=5'b01110, WB_LW=5'b01111, Error=11111;
parameter AND=3'b000, OR=3'b001, ADD=3'b010, SUB=3'b110,
NOR=3'b100, SLT=3'b111, XOR=3'b011, SRL=3'b101;
`define CPU_ctrl_signals {PCWrite, PCWriteCond, IorD, MemRead, MemWrite, IRWrite, MemtoReg, PCSource, ALUSrcB, ALUSrcA, RegWrite, RegDst, CPU_MIO, ……}
always @ (posedge clk or posedge reset)begin
……
end
always @* begin
…… 输出变量(信号)描述
…… ALU操作控制描述
end
ALU操作译码描述
数据通路控制(含ALU)
状态机

## Slide 26: State transition description
always @ (posedge clk or posedge reset)
if (reset==1) state <= IF;
else
case (state)
IF: if(MIO_ready) state <= ID;
else state <= IF;
ID: case (Inst_in[31:26])
6'b000000: state <= state <= EX_R; //R-type OP
6'b100011: state <= EX_Mem; //Lw
………………
6'b000100: state <= EX_beq; //Beq
6‘b000101: state <= EX_bne; //Bne
………………
default: state <= Error;
endcase
Mem_Ex:begin
…………
Error: state <= Error;
default: state <= Error;
endcase

## Slide 27
Output description：value should be redefined after instruction extension
always @ * begin
case(Q) //state
IF: begin ` CPU_ctrl_signals = value0; ALU_operation = ADD; end ID: begin ` CPU_ctrl_signals = value1; ALU_operation = ADD; end
EX_Mem: begin ` CPU_ctrl_signals = value2; ALU_operation = ADD; end
EX_R: begin ` CPU_ctrl_signals = value6;
case (Inst_in[5:0])
6‘b100000: ALU_operation = ???? ;
6‘b100010: ALU_operation = ???? ;
…………
default: ALU_operation <= ADD;
endcase
end
MEM_RD: begin ` CPU_ctrl_signals = value3; ALU_operation = ADD; end
WB_LW : begin ` CPU_ctrl_signals = value4; ALU_operation = ADD; end
……………………
default: begin ` CPU_ctrl_signals = value0; ALU_operation = ADD; end
endcase
R-Type

## Slide 28: ALU operation decoding for state EX_R
ALU decoder for R-format instruction
EX_R: begin ` CPU_ctrl_signals = value6;
case (Inst_in[31:26]) //R-type OP
6'b100000: ALU_operation <= ？;
6'b100010: ALU_operation <= ?;
6'b100100: ALU_operation <= ?;
6'b100101: ALU_operation <= ?;
6'b100111: ALU_operation <= ?;
6'b101010: ALU_operation <= ?;
6'b000010: ALU_operation <= ?; //SP3 shfit 1bit right
6'b000000: ALU_operation <= ?;
6'b001000: ALU_operation <=ADD; //Jr
default: ALU_operation <= ADD;
endcase
end
There is one clock delay if output and states are put together

## Slide 29
Multicycle CPU extension
Integration and substitution

## Slide 30: Controller substitution
Integration and substitution
  Substitute the following of Exp11 after correct simulation
    datapath、controller
Remove the connections from project Exp11
  Remove datapath connection
  Remove controller connection
  Replace datapath file
    M_Datapath.v
  Replace controller file
    ctrl.v文件
  In Project menu, run： Cleanup Project Files …
  Suggest to rebuild a project use Exp11 resources
    Except M_Datapath.v and ctrl.v
Exp11 Modules to be replaced Exp11

## Slide 31
Module structure after substitution
Module call relations after Exp12 datapath substitution
Datapath and controller after substitution

## Slide 32: Physical verification
使用DEMO程序目测控制器功能
  DEMO接口功能： (同实验11，代码不同)
    SW[7:5]=000， SW[2]=0(全速运行)
      SW[4:3]=00， SW[0]=0，点阵显示程序：跑马灯
      SW[4:3]=00， SW[0]=0，点阵显示程序：矩形变幻
      SW[4:3]=01， SW[0]=1，内存数据显示程序：0～F
      SW[4:3]=10， SW[0]=1，当前寄存器R9+1显示
用汇编语言设计测试程序
  测试ALU指令(R-格式译码、 Function译码)
  测试LW/SW指令(I-格式译码)
  测试分支指令(I-格式译码)
  测试转移指令(J-格式译码)

## Slide 33: DEMO interface function
SW[7:5]=显示通道选择
SW[7:5]=000：CPU程序运行输出
SW[7:5]=001：测试PC字地址
SW[7:5]=010：测试指令字
SW[7:5]=011：测试计数器
SW[7:5]=100：测试RAM地址
SW[7:5]=101：测试CPU数据输出
SW[7:5]=110：测试CPU数据输入
SW[0]=文本图形选择
SW[1]=高低16位选择
SW[2]=CPU单步时钟选择
DEMO功能，测试程序可以替换成自己的功能
SW[4:3]=00，点阵显示程序：跑马灯
SW[4:3]=00，点阵显示程序：矩形变幻
SW[4:3]=01，内存数据显示程序：0～F
SW[4:3]=10，当前寄存器+1显示
W15 SW14 SW13 SW12 SW11 SW10 SW9 SW8 SW7 SW6 SW5 SW4 SW3 SW2 SW1 SW0
LED15 LED14 LED13 LED12 LED11 LED10 LED9 LED8 LED7 LED6 LED5 LED4 LED3 LED2 LED1 LED0
X0Y3
X0Y2
X0Y1
X0Y0
X1Y3
X1Y2
X1Y1
X1Y0
X2Y3
X2Y2
X2Y1
X2Y0
X3Y3
X3Y2
X3Y1
X3Y0
X4Y3
X4Y2
X4Y1
X4Y0
MCU3
PRGO
RSTN
MCU1~2
Ardunio
SEG0
SEG1
SEG2
SEG3
SEG0
SEG1
SEG2
SEG3
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
没有使用

## Slide 34: Test program reference
设计CPU功能测试方案和测试例程
  物理调试正确后，设计测试方案与测试程序
  演示程序：简单有意义的DEMO
    修改DEMO兼有测试、自检并有一定趣味
    Project的简化版

## Slide 35
END