## Slide 1: Computer Organization & Design 实验与课程设计
Computer Organization & Design
Lab 3
Integrated SOC Design
--CPU debug and test environment

## Slide 2: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 3: Goal
1.Understand GPIO interface and device
2.Understand the organization of computer
3.Understand the relation of each part of computer
4.Understand the usage of IP core
5.Understand SOC system and implement it using IP cores

## Slide 4: Environment
Setup
  1. Computer（Intel Core i5，4GB memory）
  2. Spartan-3 Starter Kit Board/Sword
  3. Xilinx ISE14.4

## Slide 5: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 6: Task
1. Analyze interface of IP core
2. Design IP module for memory
3. Master the usage of IP core
4. Use IP core and other designed modules to implement SOC
  Top level: schematic

## Slide 7: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 8: Computer Organization
computer systems
Computer System
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……
Hardware
Software
Input: PS2
Bidirectional: Storage
Output: VGA
SW、BTN
7-Seg、LED

## Slide 9: SOC system in this course
PS2
VGA

## Slide 10: 10 modules
10 modules used in SOC
  U1： CPU -SCPU
  U2： ROM -ROM_D
  U3： RAM -RAM_B
  U4： Bus(含外设3~4) -MIO_BUS
  U5： 7-seg display interface -Multi_8CH32
  U6： 7-seg display -Seg7_Dev
  U7： GPIO and LED -PIO
  U8： clock -clk_div
  U9： Anti-jitter -Anti_jitter
  U10：Counter -Counter_x

## Slide 11: U1-CPU module：SCPU
MIPS architecture
  RISC architecture
  Three instruction types
Implemented instructions
  Include following instructions
    R-Type： add, sub, and, or, xor, nor, slt, srl*, jr, jalr, eret*；
    I-Type：addi, andi, ori, xori, lui, lw, sw, beq, bne, slti
    J-Type：J, Jal*；
IP Core- U1
  Core module: SCPU.ngc
  Interface file(empty file)：SCPU.v
  Symbol file：SCPU.sym

## Slide 12: SCPU.v
module SCPU( input wire clk,
input wire reset,
input wire MIO_ready, // Not used
input wire [31:0] inst_in, //instruction input
input wire [31:0]Data_in, //data input
output wire mem_w, //memory write control
output wire[31:0]PC_out, //PC pointer
output wire[31:0]Addr_out, //address
output wire[31:0]Data_out, //data output
output wire CPU_MIO, // Not used input wire INT //interupt
);
endmodule

## Slide 13: U2-ROM where instructions are stored：ROM_B
ROM_D/B
  Use the modules designed in lab1
  Internal memory in FPGA
    Block Memory Generator or Distributed Memory Generator
  capacity
    1024×32bit
  Symbol file：ROM_B.sym
    The symbol may need to be modified
Use the core generated in lab1
  ROM initialize：I9_mem.coe
  Core calling module: ROM_B.xco
    Linked automatically after it is generated
If there is no clk signal when using Distributed Memory Generator, please delete ”clka” pin

## Slide 14: Call ROM_B
ROM interface
ROM_B U2 ( .clka(clk_m), //存储器时钟，与CPU反向
.addra(PC_out[11:2]), // ROM地址PC指针，来自CPU
.douta(inst[31:0]) // ROM输出作为指令输入CPU
);
Graphical input
  ROM_B.sym
Core calling does not require empty file
  Interface file

## Slide 15: U3-data strorage：RAM_B
RAM_B
  Internal memory of FPGA
    Block Memory Generator
  capacity
    1024×32bit
  Symbol file：RAM_B.sym
    Required modification
Use core generated in lab1
  RAM initialization：D_mem.coe
  Core calling : RAM_B.xco
    Linked automatically after it is generate

## Slide 16: Calling RAM_B
RAM interface
RAM_B U3 ( .clka(clk_m), // 存储器时钟，与CPU反向
.wea(data_ram_we), // 存储器读写，来自MIO_BUS
.addra(ram_addr), // 地址线，来自MIO_BUS
.dina(ram_data_in), // 输入数据线，来自MIO_BUS
.douta(ram_data_out) // 输出数据线，来自MIO_BUS
);
Graphical input
  RAM_B.sym
Core calling does not require empty file

## Slide 17: U4-BUS：MIO_BUS
MIO_BUS
  The interface between CPU and data
Function
  Data storage、the interface of 7-Seg、 SW、BTN and LED
In this lab, we use soft IP core U4
  Core calling MIO_BUS.ngc
  Interface file：MIO_BUS_IO.v
  symbol：MIO_BUS.sym

## Slide 18: IO BUS module-MIO_BUS.v
module MIO_BUS( input wire clk, input wire rst,
input wire [3:0] BTN, input wire [15:0]SW,
input wire mem_w,
input wire [31:0] Cpu_data2bus, //data from CPU
input wire [31:0] addr_bus, //addr from CPU
input wire [31:0] ram_data_out,
input wire [15:0] led_out,
input wire [31:0] counter_out,
input wire counter0_out,
input wire counter1_out,
input wire counter2_out,
output wire [31:0] Cpu_data4bus, //write to CPU
output wire [31:0] ram_data_in, //from CPU write to Memory
output wire [9: 0] ram_addr, //Memory Address signals
output wire data_ram_we,
output wire GPIOf0000000_w, // GPIOffffff00_we
output wire GPIOe0000000_we, // GPIOfffffe00_we
output wire counter_we, //记数器
output wire [31:0] Peripheral_in //送外部设备总线
);
endmodule

## Slide 19: Signals of MIO_BUS module
MIO_BUS U4( clk_50M, //主板时钟
botton_out[3], //复位，按钮BTN3
BTN [3:0] , //4位原始按钮输入
SW [7:0], //8位原始开关输入
mem_w, //存储器读写操作，来自CPU
Cpu_data2bus [31:0] , //CPU输出数据总线
addr_bus [31:0] , //地址总线，来自CPU
ram_data_out [31:0] , //来自RAM数据输出
led_out [7:0], //来自LED设备输出
counter_out [31:0] , //当前通道计数输出，来自计数器外设
counter0_out, //通道0计数结束输出，来自计数器外设
counter1_out, //通道1计数结束输出，来自计数器外设
counter2_out, //通道2计数结束输出，来自计数器外设
Cpu_data4bus [31:0] , //CPU写入数据总线，连接到 CPU
ram_data_in [31:0] , //RAM 写入数据总线，连接到RAM
ram_addr [9: 0] , //RAM访问地址，连接到RAM
data_ram_we, //RAM读写控制， 连接到RAM
GPIOf0000000_w, // 设备一LED写信号
GPIOe0000000_we, // 设备二7段写信号，连接到U5
counter_we, //记数器写信号，连接到U10
Peripheral_in [31:0] //外部设备写数据总线，连接所有写设备
);
endmodule

## Slide 20
GPIO interface module

## Slide 21: U7-GPIO device interface 1-- SPIO
Device GPIO
& LED
clk_io
GPIOf0000000_we
Peripheral_in
8-LED
led_out
Counter_set
GPIOf0
rst
22位
GPIO output device
  address=f0000000 - ffffffff0 (ffffff00-ffffffff0)
  Read/write control signal：GPIOf0000000_we(GPIOffffff00_we)
  {GPIOf0[21:0],LED,counter_set}
Function
  LEDs and counter 控制器读写
  可回读，检测状态
In this lab, we use soft IP core- U7
  Core calling: SPIO.ngc
  interface file：SPIO_IO.v
  symbol：SPIO.sym

## Slide 22: Interface file -SPIO.v
  module SPIO(input clk, //io_clk，与CPU反向
  input rst,
  input EN, //来自U4
  input [31:0] P_Data, //来自U4
  input Start //串行输出启动
  output [1:0] counter_set, //来自U7，后继用
  output [15:0] led_out, //输出到LED,回读到U4
  output [23:0] GPIOf0 //备用
  output led_clk, //串行时钟
  output led_sout, //串行LEDE值
  output LED_PED, //LED使能
  output led_clrn //LED清零
  );
  endmodule

## Slide 23: U6-GPIO device 2： Seg7_Dev
7-seg display module
  Connect to CPU through Multi_8CH32
  address=E0000000 - EFFFFFFF (FFFFFE00-FFFFFEFF)
Function (refer to lab2)
Use soft IP core - U5
  SSeg7_Dev.ngc
  SSeg7_Dev.v
  SSeg7_Dev.sym

## Slide 24: Interface file ~Seg7_Dev.v
  module SSeg7_Dev(input clk, //时钟
  input rst, //复位
  input Start, //串行扫描启动
  input SW0, //文本(16进制)/图型(点阵)切换
  input flash, //七段码闪烁频率
  input[31:0]Hexs, //32位待显示输入数据
  input[7:0]point, //七段码小数点：8个
  input[7:0]LES, //七段码使能：=1时闪烁
  output seg_clk, //串行移位时钟
  output seg_sout, //七段显示数据(串行输出)
  output SEG_PEN, //七段码显示刷新使能
  output seg_clrn //七段码显示清零
  );
  endmodule
  module Seg7_Dev(input wire [31:0] disp_num, //来自U5
  input wire [1:0]SW, //来自U9
  input wire flash_clk, //通用分频器
  input wire [1:0] Scanning, //来自U8
  input wire [3:0] pointing, //来自U5
  input wire [3:0] blinking, //来自U5
  output wire [3:0] AN,
  output reg [7:0] SEGMENT ); //来自U5
  endmodule

## Slide 25: U5- Interface module Multi_8CH32
GPIO
Multi_8CH32
clk_io
GPIOe0000000_we
Peripheral_in
Seg7 Device
disp_num
rst
…
Test_data0
Test_data7
…
Peripheral_in
GPIO output interface module
  address=E0000000 - EFFFFFFF (FFFFFE00-FFFFFEFF)
  Read/write control signal：GPIOe0000000_we(GPIOfffffe00_we)
Function (refer to Exp02)
  Data0 as the display interface
    GPIOe0000000_we=1
    CLK positive edge
  Data1-data7: debug signal
Use soft IP core U6
  核调用模块Multi_8CH32.ngc
  核接口信号模块(空文档)： Multi_8CH32_IO.v
  核模块符号文档：Multi_8CH32.sym

## Slide 26: Interface file -Multi_8CH32_IO.v
  module Multi_8CH32 ( input clk, //io_clk，同步CPU
  input rst,
  input EN, //=1, 通道0显示
  input[63:0]point_in, //针对8个显示通道各8个小数点
  input[63:0]blink_in, //针对8个通道各8位闪烁控制
  input [2:0] Test, //通道选择SW[7:5]
  input [31:0] Data0, //通道0
  input [31:0] data0, //通道1
  input [31:0] data1, //通道2
  input [31:0] data2, //通道3
  input [31:0] data3, //通道4
  input [31:0] data4, //通道5
  input [31:0] data5, //通道6
  input [31:0] data6, //通道7
  output reg[3:0] point_out, //小数点输出
  output reg[3:0] blink_out, //闪烁控制输出
  output [31:0] disp_num //接入7段显示器
  );
  endmodule

## Slide 27: Signals of Multi_8CH32
  Multi_8CH32 U5( .clk(clk_io), .rst(rst),
  . EN(GPIOe0000000_we), //来自U4
  . point_in(point_in), //外部输入
  .blink_in(blink_in), //外部输入
  .Test(SW_OK[7:5]), //来自U9
  .Data0(Peripheral_in), //来自U4
  .data1({2‘b00,PC_out[31:2]}), //来自U1
  .data2(counter_out), //来自U10
  .data3(Inst), //Inst，来自CPU
  .data4(addr_bus), //来自CPU
  .data5(Cpu_data2bus), //来自CPU
  .data6(Cpu_data4bus), //来自CPU
  .data7(PC_out), //来自CPU;
  .point_out(point_out), //输出到U6
  .blink_out(blink_out), //输出到U6
  .disp_num(disp_num) //输出到U6
  );

## Slide 28: GPIO device interface 3,4: Device_GPIO_SW_BTN
8-bits Switch and 4-bits Button input
  address= f0000000-ffffffff0，A[2]=0
  These two devices are included in U4，MIO_BUS
  Relation with CPU data bus（when addre_bus=f0000000）
Cpu_data4bus = {counter0_out, counter1_out, counter2_out, 1'h000, BTN,SW};
CPU
clk_io
Cpu_data4bus
addre_bus=f0000000
Led out
BTN
SW
mem_w=0

## Slide 29: U10-peripheral device 5: Counter_x.v
General counter，
  address=F0000004 – FFFFFFF4 (FFFFFF04-FFFFFFF4)
  r/w control：counter_we
Function
  3 paths independent counter
  Output for choose path or initialization
    counter_set=00、01、10 for path0、1、2
    counter_set=11对应计数通道工作设置
Use soft IP core- U10
  核调用模块Counter_x.ngc
  核接口信号模块(空文档)：Counter_x.v
  核模块符号文档：Counter_x.sym

## Slide 30: Interface file -Counter_x.v
module Counter_x(input clk, //io_clk
input rst,
input clk0, //clk_div[7]，来自U8
input clk1, // clk_div[10]，来自U8
input clk2, //clk_div[10]，来自U8
input counter_we, //计数器写控制，来自U4
input [31:0] counter_val, //计数器输入数据，来自U4
input [1:0] counter_ch, //计数器通道控制，来自U7
output counter0_OUT, //输出到U4
output counter1_OUT, //输出到U4
output counter2_OUT, //输出到U4
output [31:0] counter_out //输出到U4
);
endmodule

## Slide 31
SOC auxiliary modules
U8：clk_div
U9：anti-jitter
Refer to previous lab

## Slide 32: clk_div.v
module clk_div(input clk,
input rst,
input SW2,
output [31:0]clkdiv,
output Clk_CPU
);
endmodule

## Slide 33: Anti_jitter.v
  module SAnti_jitter(input clk, //主板时钟
  input RSTN
  input readn //阵列式键盘读
  input [3:0]Key_y, //阵列式键盘列输入
  output reg[4:0] Key_x, //阵列式键盘行输出
  output reg[4:0] Key_out,//阵列式键盘扫描码
  output reg Key_ready, //阵列式键盘有效
  input [15:0] SW, //开关输入
  output reg [3:0] ] BTN_OK,//列按键输出
  output reg [3:0] pulse, //列按键脉冲输出
  output reg [15:0] SW_OK, //开关输出
  output reg CR, //RSTN短按输出
  output reg rst //复位， RSTN长按输出
  );
  endmodule

## Slide 34: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 35: Project ：OExp03-IP2SOC
Build platform for CPU debug and application
  Use schematic implementation on top，call IP core
    File name：Top_OExp03_IP2SOC.sch
SOC platform
  Use the modules in lab1 and lab2 and given IP cores.
    CPU (given IP core)：U1
    ROM (ISE IP 核)：U2
    RAM (ISE IP核)：U3
    Bus (given IP核)：U4
    Multiplexer(lab1 Multi_8CH32)：U5
    7-seg display(lab2 SSeg7_Dev IP)：U6
    LED display (lab2 SPIO)：U7
    Clock (clk_div)：U8
    Anti-jitter (IP核)：U9
    Data input (IP核)：M4(no use for the moment)

## Slide 36: Create SOC project
  Start ISE software
  File New Project，type project name：OExp03-IP2SOC or Top_Simple_CPU_App
  Next, next, finish
This project is shared by following experiment: a simple implementation of CPU

## Slide 37: SOC project

## Slide 38
Copy symbol files of U1~U10 to current project
Copy .ngc files of U1~U10 to current project

## Slide 39
SOC top level: schematic
--add U1、U2、U3、U4 and U10 based on lab2

## Slide 40: SOC schematic

## Slide 42: Add modules

## Slide 43: Add CPU module

## Slide 44: Add more modules and connect

## Slide 45: Finish
CPU核

## Slide 46: Check schematic

## Slide 47: Link to modules
连接模块的接口信号
  模块放置后根据顶层分解图连接各模块
  信号连线时注意各信号之间的合理布线距离
    当连线较近时注意不要同时选中多个信号节点：NET
顶层调用模块关联
  顶层窗口放置模块Symbol后会直接调用对应模块
  建立核端口模块与软核模块关联
    只有端口信号的模块，没有逻辑代码的空文档.v
      综合器会根据端口模块连接信号
  Click “Add Source”, choose the corresponding .v file

## Slide 48
Memory IP core reinitialize

## Slide 49: ROM_B reinitialize
Use I9_men.coe to initialize ROM
In Design window, double click U2
  Double click ROM_B
    Or select ROM_B
    In Processes Running windown double click Manager Core
  In manage cores window, click Next
  Core is generated

## Slide 50
  〖第四步〗link to initialize file to generate ROMIP core
    Click Next，skip page 2, page 3 pop up
    Click“Browse...” choose I9_men.coe
    Click Generate to generate ROM core
点击查验
点击Browse关联 Init File
最后点击生成
查看Datasheet
I9_men.coe

## Slide 51: ROM initialization file：.coe
ROM.coe format
  Can be open and edit in ISE or other text editor
  format：
    Line 1：initialization_radix is HEX（also can be binary）
    Line 2：initialization vector
    Start line 3：elements of initialization, separated by “,” and ended with ”;”
    Add Comment with“#”at beginning or ending of the file，not allowed in the midddle
  memory_initialization_radix=16;
  memory_initialization_vector=
  00000827, 0001102a, 00421820, 00622020, 00832820, 00a43020,
  00c53820, 00e64020, 01074820, 01285020, 01495820, 016a6020,
  018b6820, 01ac7020, 01cd7820, 01ee8020, 020f8820, 02309020,
  02519820, 0272a020, 0293a820, 02b4b020, 02d5b820, 02f6c020,
  0317c820, 0338d020, 0359d820, 037ae020, 039be820, 03bcf020,
  03ddf820, 08000000;
The above data is some test instructions
  Used in CPU simulation
  Use I9_mem.coe when downloading to board

## Slide 52: Simple test instructions
#baseAddr 0000
loop: nor r1,r0,r0; //r1=FFFFFFFF
slt r2,r0,r1; //r2=00000001
add r3,r2,r2; //r3=00000002
add r4,r3,r2; //r4=00000003
add r5,r4,r3; //r5=00000005
add r6,r5,r4; //r6=00000008
add r7,r6,r5; //r7=0000000d
add r8,r7,r6; //r8=00000015
add r9,r8,r7; //r9=00000022
add r10,r9,r8; //r10=00000037
add r11,r10,r9; //r11=00000059
add r12,r11,r10; //r12=00000090
add r13,r12,r11; //r13=000000E9
add r14,r13,r12; //r14=00000179
add r15,r14,r13; //r15=00000262
add r16,r15,r14; //r16=000003DB
add r17,r16,r15; //r17=000006D3
add r18,r17,r16; //r18=00000A18
add r19,r18,r17; //r19=000010EB
add r20,r19,r18; //r20=00001B03
add r21,r20,r19; //r21=00003bEE
add r22,r21,r20; //r22=000046F1
add r23,r22,r21; //r23=000080DF
add r24,r23,r22; //r24=0000C9D0
add r25,r24,r23; //r25=00014AAF
add r26,r25,r24; //r26=0001947F
add r27,r26,r25; //r27=0012DF2E
add r28,r27,r26; //r28=001473AD
add r29,r28,r27; //r29=002752DB
add r30,r29,r28; //r30=003BC688
add r31,r30,r29; //r31=00621963
j loop;

## Slide 53: RAM_B initialize
Same as ROM, click Next, enter page 4
  〖step 4〗link to initialization file (D_men.coe) to generate RAM IP core
点击查验
点击选中Load Init File
最后点击生成
查看Datasheet
点击Browse关联 Init File

## Slide 54: RAM initialization file --.coe
D_mem.coe
memory_initialization_radix=16;
memory_initialization_vector=
f0000000, 000002AB, 80000000, 0000003F, 00000001, FFF70000, 0000FFFF, 80000000, 00000000, 11111111, 22222222, 33333333, 44444444, 55555555, 66666666, 77777777, 88888888, 99999999, aaaaaaaa, bbbbbbbb, cccccccc, dddddddd, eeeeeeee, FFFFFFFF, 557EF7E0, D7BDFBD9, D7DBFDB9, DFCFFCFB, DFCFBFFF, F7F3DFFF, FFFFDF3D, FFFF9DB9, FFFFBCFB, DFCFFCFB, DFCFBFFF, D7DB9FFF, D7DBFDB9, D7BDFBD9, FFFF07E0, 007E0FFF, 03bdf020, 03def820, 08002300;
Can be used for simulation and verification on board
Red data is for LED graphics

## Slide 55
SOC physical verification
-just use demo to test functions

## Slide 56: DEMO interface
SW[7:5]=choose datapath
SW[7:5]=000：output when CPU runs the program
SW[7:5]=001：PC word address
SW[7:5]=010：instruction word
SW[7:5]=011：counter
SW[7:5]=100：RAM address
SW[7:5]=101：CPU data output
SW[7:5]=110：CPU data input
SW[0]=text/graphics
SW[1]=upper/lower 16-bits
SW[2]=CPU_clk
SW[4:3]=00，display bit-map：marquee
SW[4:3]=00，display bit-map：matrix transform
SW[4:3]=01，display memory data：0～F
SW[4:3]=10，display current reg+1
W15 SW14 SW13 SW12 SW11 SW10 SW9 SW8 SW7 SW6 SW5 SW4 SW3 SW2 SW1 SW0
LED15 LED14 LED13 LED12 LED11 LED10 LED9 LED8 LED7 LED6 LED5 LED4 LED3 LED2 LED1 LED0
X0Y3
X0Y2
X0Y1
X0Y0
X1Y3
X1Y2
X1Y1
X1Y0
X2Y3
X2Y2
X2Y1
X2Y0
X3Y3
X3Y2
X3Y1
X3Y0
X4Y3
X4Y2
X4Y1
X4Y0
MCU3
PRGO
RSTN
MCU1~2
Ardunio
SEG0
SEG1
SEG2
SEG3
SEG0
SEG1
SEG2
SEG3
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
No use

## Slide 57: SOC verification
Simulation
  Do Simulations for your own designed modules
SOC verification
  Download .bit file
  verify SOC functions
  observe SOC key signals
    Substitute I9_mem.coe by test data

## Slide 58: Switch settings
Graphics test
文本功能测试
开关 | 位置 | 功能
SW[1:0] | X0 | 7-seg graphical display
SW[2] | 0 | CPU high frequency clock
SW[4:3] SW[4:3] | 00 11 | Light of 7-seg shift right from top down Each bit of Big Rectangle of 7-seg lights in order
SW[7:5] | 000 | For peripherals（E0000000/FFFFFE00）
开关 | 位置 | 功能
SW[1:0] | 01 11 | Display text on 7-seg (lower 16-bits) Display text on 7-seg (upper 16-bits)
SW[2] | 0 | CPU high frequency clock
SW[4:3] SW[4:3] | 01 10 | Display RAM number on 7-seg Display add on 7-seg
SW[7:5] | 000 | For peripherals（E0000000/FFFFFE00）

## Slide 59: Qualitative observation
SOC signal test
  CPU high speed running
  Test switch setting
开关 | 位置 | 功能
SW[1:0] | 01 | Display text on 7-seg (lower 16-bits)
SW[1:0] | 11 | Display text on 7-seg (upper 16-bits)
SW[2] | 0 | CPU high speed clk
SW[7:5] | 010 | Counter output
SW[7:5] | 100 | CPU数据存储地址addr_bus（ALU）
SW[7:5] | 101 | CPU数据输出Cpu_data2bus (寄存器B)
SW[7:5] | 110 | CPU数据输入Cpu_data4bus(RAM输出)

## Slide 60: Qualitative observation
SOC信号测试
  CPU low speed running
  Test switch settings
  Use test data to substitute DEMO *
开关 | 位置 | 功能
SW[1:0] | 01 | 七段码文本显示（低16位）
SW[1:0] | 11 | 七段码文本显示（高16位）
SW[2] | 1 | CPU单步时钟
SW[7:5] | 001 | CPU指令字地址PC_out[31:2]
SW[7:5] | 011 | ROM指令输出Inst_in
SW[7:5] | 100 | CPU数据存储地址addr_bus(ALU输出)
SW[7:5] | 101 | CPU数据输出Cpu_data2bus(寄存器B)
SW[7:5] | 110 | CPU数据输入Cpu_data4bus(RAM输出)
SW[7:5] | 111 | CPU指令字节地址PC_out

## Slide 61
END