## Slide 1: Computer Organization & Design
Computer Organization & Design
Lab 4
Substitute CPU core
-IP core design CPU/IP2CPU

## Slide 2: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 3: Environment
Setup
  1. Computer（Intel Core i5，4GB memory）
  2. Spartan-3 Starter Kit Board/Sword
  3. Xilinx ISE14.4

## Slide 4: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 5: Task
1. Design CPU using IP cores and substitute CPU core in lab 3
  Implement integrated CPU using given IP cores
3. Design datapath unit and do simulation：
  ALU
  Register Files
4. Master the usage of IP cores

## Slide 6: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 7: Computer Organization
Decomposability of computer systems
Computer System
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……
Hardware
Software
Input: PS2
Bidirectional: Storage
Output: VGA
SW、BTN
7-Seg、LED

## Slide 8: Digital circuits vs CPU organization
Digital circuit
  General circuits that controls logical event with logical gates --Hardware
Computer organization
  Special circuits that processes logical action with instructions -Software
Control unit
Datapath
Control signals
Status signals
Control output
Data input
Data output
Status input

## Slide 9: CPU part 1-datapath：Data_path
Data_path
  Main part of CPU
  Control target of Register transfer： general data path
Function
  Calculation
  General registers
  General counting
Soft IP cores- Data_path
  Core Module: Data_path.ngc
  Interface file(empty file) ：Data_path.v
  Symbol file：Data_path.sym

## Slide 10: Data_path.v
module Data_path( input clk, //寄存器时钟
input rst, //寄存器复位
input[25:0]inst_field, //指令数据域
input RegDst,
input ALUSrc_B,
input MemtoReg,
input Jump,
input Branch,
input RegWrite,
input[31:0]Data_in,
input[2:0]ALU_Control,
output[31:0]ALU_out,
output[31:0]Data_out,
output[31:0]PC_out
);
endmodule

## Slide 11: CPU part 2-controller：SCPU_ctrl
SCPU_ctrl
  Main part of CPU
  Arithmetic and path controller in register transfer
Function
  Instruction decoder
  Generate operation control signal： ALU arithmetic and logic control
  Generate instruction required path
Soft IP core- SCPU_ctrl
  Core module: SCPU_ctrl.ngc
  Interface file(empty file) ：SCPU_ctrl.v
  Symbol file：SCPU_ctrl.sym

## Slide 12: SCPU_ctrl.v
module SCPU_ctrl( input[5:0]OPcode, //OPcode
input[5:0]Fun, //Function
input MIO_ready, //CPU Wait
output reg RegDst,
output reg ALUSrc_B,
output reg MemtoReg,
output reg Jump,
output reg Branch,
output reg RegWrite,
output reg mem_w,
output reg [2:0]ALU_Control,
output reg CPU_MIO
);
endmodule

## Slide 13: Data path part 1：ALU
Implement 5 operations
  Based on ALU in logic lab
  Schematic type
  simulation
Zero
Result
Overflow
A
B
Alu Operation
ALU Control Lines | Function | note
000 | And | 兼容
001 | Or | 兼容
010 | Add | 兼容
110 | Sub | 兼容
111 | Set on less than | 
100 | nor | 扩展
101 | srl | 扩展
011 | xor | 扩展

## Slide 14: HDL code
module alu(input A, B,
input[2:0] ALU_operation,
output[31:0] res,
input zero, overflow);
wire [31:0] res_and,res_or,res_add,res_sub,res_nor,res_slt;
reg [31:0] res;
parameter one = 32'h00000001, zero_0 = 32'h00000000;
assign res_and = A&B;
assign res_or = A|B;
assign res_add = A+B;
assign res_sub = A-B;
assign res_slt =(A < B) ? one : zero_0;
always @ (A or B or ALU_operation)
case (ALU_operation)
3'b000: res=res_and;
3'b001: res=res_or;
3'b010: res=res_add;
3'b110: res=res_sub;
3'b100: res=~(A | B);
3'b111: res=res_slt;
default: res=32'hx;
endcase
assign zero = (res==0)? 1: 0;
endmodule
How do you write with overflow code ?
always @ (*)
case (ALU_operation)
3'b000: res=A&B;
3'b001: res=A|B;
3'b010: res=A+B;
3'b110: res=A-B;
3'b100: res=~(A | B);
3'b111: res=(A < B) ? one : zero_0;
default: res=32'hx;
endcase
What is the difference The codes in the Synthesize?

## Slide 15: Digital system part：Register files
Implement 32×32bit register files
  Optimize the Regs unit in logic lab
  Use behavioral description and do simulation
Ports
  Two read pins：
    R_addr_A
    R_addr_B
  One write pin, with write signal
    Wt_addr
    L_S

## Slide 16: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 17: project：OExp04-IP2CPU
Decompose CPU into two IP cores
  Build CPU based on Exp03 using two IP cores
  Top level is same as that of Exp03
    Top_OExp04_IP2CPU.sch
Logic modules optimization
  Optimize ALU module
  Optimize Register Files
  Objective: meet MIPS processor requirements

## Slide 18: 设计要点
Build CPU using IP core

## Slide 19: Reorganize Exp03 project
Remove CPU core in project
  Delete core link
Delete core files
  SCPU.ngc 和 SCPU.v
  In Project menu, run: Cleanup Project Files …
Rebuild project using Exp03 resources
  Remove CPU core
  rename：OExp04-IP2CPU
Delete

## Slide 20
Copy SCPU_ctrl.sym、Data_path.sym to current project
Copy SCPU_ctrl.ngc、Data_path.ngc to current project
Interface files: SCPU_ctrl.v、Data_path.v

## Slide 21: CPU design: schematic

## Slide 22
Module calling relation after CPU design

## Slide 23
design ALU in schematic way
此部件是逻辑实验的ALU进一步改造供Exp05使用
为了减少相互影响请单独建立工程

## Slide 24: Schematic input
信号扩展模块
注意：加减器做减法时用补码是±31位
为了和无符号加法兼容需要扩展符号位
定制符号
非标准件

## Slide 25
Copy the following symbol files to ALU project：
（provided in Exp01）
and32、or32、ADC32、xor32、nor32、srl32、SignalExt_32、mux8to1_32、or_bit_32

## Slide 26: ALU simulation code
A=32'hA5A5A5A5;
B=32'h5A5A5A5A;
ALU_operation =3'b111;
#100;
ALU_operation =3'b110;
#100;
ALU_operation =3'b101;
#100;
ALU_operation =3'b100;
#100;
ALU_operation =3'b011;
#100;
ALU_operation =3'b010;
#100;
ALU_operation =3'b001;
#100;
ALU_operation =3'b000;
#100;
A=32'h01234567;
B=32'h76543210;
ALU_operation =3'b111;
ALU模块调用结构
仿真通过后封装逻辑符号

## Slide 27: ALU_Simulation result

## Slide 28: RTL-Schematic

## Slide 29
Design Register files
Using Behaviral description 此部件是逻辑实验Exp10的Regs的优化供Exp05使用
可与ALU共享工程
逻辑Exp10的Regs特点：
采用逻辑门实例描述实现D触发器
采用多层调用MB_DFF触发器模块实现寄存器
采用结构描述实现Register Files

## Slide 30
Code reference
Module regs(input clk, rst, L_S,
input [4:0] R_addr_A, R_addr_B, Wt_addr,
input [31:0] wt_data
output [31:0] rdata_A, rdata_B
);
reg [31:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (Rs_addr_A == 0) ? 0 : register[reg_Rd_addr_A]; // read
assign rdata_B = (Rt_addr_B == 0) ? 0 : register[reg_Rt_addr_B]; // read
always @(posedge clk or posedge rst)
begin if (rst==1) for (i=1; i<32; i=i+1) register[i] <= 0; // reset
else if ((Rd_addr != 0) && (we == 1))
register[Wt_addr] <= wdata; // write
end
endmodule
代码来自李亚民教授
Note that there is BUG in this code
仿真通过后封装逻辑符号

## Slide 31: Regfile simulation

## Slide 32: Verification-DEMO interface
Same as lab3
SW[7:5]=choose datapath
SW[7:5]=000：output when CPU runs the program
SW[7:5]=001：PC word address
SW[7:5]=010：instruction word
SW[7:5]=011：counter
SW[7:5]=100：RAM address
SW[7:5]=101：CPU data output
SW[7:5]=110：CPU data input
SW[0]=text/graphics
SW[1]=upper/lower 16-bits
SW[2]=CPU_clk
SW[4:3]=00，display bit-map：marquee
SW[4:3]=00，display bit-map：matrix transform
SW[4:3]=01，display memory data：0～F
SW[4:3]=10，display current reg+1
W15 SW14 SW13 SW12 SW11 SW10 SW9 SW8 SW7 SW6 SW5 SW4 SW3 SW2 SW1 SW0
LED15 LED14 LED13 LED12 LED11 LED10 LED9 LED8 LED7 LED6 LED5 LED4 LED3 LED2 LED1 LED0
X0Y3
X0Y2
X0Y1
X0Y0
X1Y3
X1Y2
X1Y1
X1Y0
X2Y3
X2Y2
X2Y1
X2Y0
X3Y3
X3Y2
X3Y1
X3Y0
X4Y3
X4Y2
X4Y1
X4Y0
MCU3
PRGO
RSTN
MCU1~2
Ardunio
SEG0
SEG1
SEG2
SEG3
SEG0
SEG1
SEG2
SEG3
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
No use

## Slide 33: Thinking
How to add “overflow” function for ALU?
  Hint：analyze the sign of the calculation result
Analyze Register Files design of logic Exp10
  What optimization have you done in this lab？
  What is the problem if we use Register Files of logic Exp10 directly?

## Slide 34
END