## Slide 1: Computer Organization & Design 实验与课程设计
Asso. Prof. Shi Qingsong
College of Computer Science and Technology, Zhejiang University
zjsqs@zju.edu.cn
Computer Organization & Design
Lab 9
Multi-cycle IP core integrated CPU
--build multi-cycle CPU debugging、test and application environment

## Slide 2: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 3: Course Outline
Environment
Task
Principles
Implementation
Notes:   Rudimentary logic functions=基本的逻辑函数

## Slide 4: Task
1. Build testing environment for CPU multicycle implementation
  Rebuild Exp03 top module using structural description
    Substitute CPU core using multicycle implementation
2. Substitute CPU core using datapath core and controller core
    reuse modules of Exp03 except CPU

## Slide 5: Course Outline
Environment
Task
Principal
Implementation

## Slide 6: CPU organization
Digital circuit
  General circuits that controls logical event with logical gates --Hardware
Computer organization
  Special circuits that processes logical action with instructions -Software
Control unit
Datapath
Control signals
Status signals
Control output
Data input
Data output
Status input

## Slide 7: Computer Organization
Decomposability of computer systems
Computer System
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……
Hardware
Software
Input: PS2
Bidirectional: Storage
Output: VGA
SW、BTN
7-Seg、LED

## Slide 8: 多周期处理器测试框架或SOC
Different from simple implementation
无ROM

## Slide 9: 9 modules
Use 9 modules to build SOC test framework
  U1： MCPU -Muliti-CPU
  U2： ROM -ROM_D
  U3： RAM -RAM_B
  U4： Bus(含外设3~4) -MIO_BUS
  U5： 7-seg display interface -Multi_8CH32
  U6： 7-seg display -Seg7_Dev
  U7： GPIO and LED -PIO
  U8： clock -clk_div
  U9： Anti-jitter -Anti_jitter
  U10：Counter -Counter_x
以上除U1外与单周期共享

## Slide 10: U1-CPU module：Multi-CPU
MIPS ISA
  RISC
  Three instruction formats
SOC test module
  Consists of two IP cores: datapath and controller
    Can be integrated directly with 2 IP cores
    Or first use CPU IP core
      Then use 2 IP cores after debugging
  This lab can use IP Core- U1
    Core module: Multi_CPU.ngc
    interface：Multi_CPU.v
    symbol：Multi_SCPU.sym

## Slide 11: CPU core interface-Multi_CPU.v
module Muliti_CPU ( input wire clk,
input wire reset,
input wire MIO_ready, // be used：=1
output wire[31:0]PC_out, //Test
output[31:0] inst_out, //TEST
output wire mem_w, //存储器读写控制
output wire[31:0]Addr_out,//数据空间访问地址
output wire[31:0]Data_out//数据输出总线
input wire [31:0]Data_in, //数据输入总线
output wire CPU_MIO, // Be used input wire INT //中断
output[4:0]state //Test
);
endmodule
注意与单周期区别

## Slide 12: CPU unit 1-- datapath：M_datapath
This lab use IP soft core- M_datapath
  Core module: M_atapath.ngc
  interface：M_datapath.v
  symbol：M_datapath.sym
Important signals:
  Inst：output of instruction register
  PC_Current：current PC(PC+4)
  M_addr：memory address
  Branch(beq in textbook)：
    =1：beq
    =0：bne
  PCWriteCond：Branch instruction
MUX选择更多输入以兼容扩展

## Slide 13: M_datapath.v
module M_datapath(input clk,
input reset,
input MIO_ready, //=1
input IorD,
input IRWrite,
input[1:0] RegDst, //预留到2位
input RegWrite,
input[1:0]MemtoReg, //预留到2位
input ALUSrcA,
input[1:0]ALUSrcB,
input[1:0]PCSource, //4选1控制
input PCWrite,
input PCWriteCond,
input Branch,
input[2:0]ALU_operation,
output[31:0]PC_Current,
input[31:0]data2CPU,
output[31:0]Inst,
output[31:0]data_out,
output[31:0]M_addr,
output zero,
output overflow
);
endmodule

## Slide 14: CPU unit 2-- controller：ctrl
This lab use IP soft core- ctrl
  Core module: ctrl.ngc
  Interface file：ctrl.v
  symbol：ctrl.sym
Important signals:
  MIO_ready：I/O is ready
    =0 CPU wait
    =1 CPU execute
    Always be 1 in this lab
  Inst_in：instruction input，coming from IR output
  State_out：state codes，for test

## Slide 15: Controller interface- ctrl.v
module ctrl(input clk,
input reset,
input [31:0] Inst_in,
input zero,
input overflow,
input MIO_ready,
output reg MemRead,
output reg MemWrite,
output reg[2:0]ALU_operation,
output [4:0]state_out,
output reg CPU_MIO,
output reg IorD,
output reg IRWrite,
output reg [1:0]RegDst,
output reg RegWrite,
output reg [1:0]MemtoReg,
output reg ALUSrcA,
output reg [1:0]ALUSrcB,
output reg [1:0]PCSource,
output reg PCWrite,
output reg PCWriteCond,
output reg Branch
);
endmodule

## Slide 16: U3-Instructions storage：RAM_B
RAM_B
  Combine ROM and RAM of Lab3
    Instruction and data share the same RAM
  FPGA internal memory
    Block Memory Generator or Distributed Memory Generator
  Same Capacity with RAM_B of lab 3
    1024×32bit
  symbol：RAM_B.sym
    Automatically generated one needs to be adjusted
In this lab, IP core should be generated again
  RAM initialization file：mem.coe
    Instructions and data are in the same memory
  Core module: RAM_B.xco
    Automated connected after generated，empty file is not needed
用Distributed Memory Generator没有clk信号
请编辑删除clka引脚。SP3平台用不用

## Slide 17: RAM_B is called in the same way as Lab3
ROM interface
RAM_B U3 ( .clka(clk_m), //存储器时钟，与CPU反向
.addra(ram_addr[9:0]), // RAM地址指针,来自MIO_BUS
.douta(ram_data_out) // RAM输出,代码或数据
);
Graphical symbol
  RAM_B.sym
Empty file is not required
红色与单周期不同均通过MIO_BUS

## Slide 18: U3-memory initialization file：mem.coe
memory_initialization_radix=16;
memory_initialization_vector=
3c03f000, 2014003f, 3c088000, 00632020, 20020001, 00000827, 00205020, 20070003, 00e73827, 20067fff,
00008820, 200502ab, ac650000, 20120002, ac600004, 8c650000, 00a52820, 00a52820, ac650000, ac660004,
3c0dffff, 8c650000, 00a52820, 00a52820, ac650000, 8c650000, 00a85824, 21ad0001, 11680015, 8c650000,
20120018, 00b25824, 11600005, 1172000a, 20120008, 1172000b, ac890000, 08000015, 11410001, 0800002a,
00005027, 014a5020, ac8a0000, 08000015, 8e2902a0, ac890000, 08000015, 8e290260, ac890000, 08000015,
3c0dffff, 014a5020, 01425025, 22310004, 02348824, 21290001, 11210001, 0800003b, 21290005, 8c650000,
00a55820, 016b5820, ac6b0000, ac660004, 8c650000, 00a85824, 1168fffd, 0800001d, 00000000, 00000000,
00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000, 00000000,
………………
………………
f0000000, 000002AB, 80000000, 0000003F, 00000001, FFFF0000, 0000FFFF, 80000000, 00000000, 11111111, 22222222, 33333333, 44444444, 55555555, 66666666, 77777777, 88888888, 99999999, aaaaaaaa, bbbbbbbb, cccccccc, dddddddd, eeeeeeee, ffffffff, 557EF7E0, D7BDFBD9, D7DBFDB9, DFCFFCFB, DFCFBFFF, F7F3DFFF, FFFFDF3D, FFFF9DB9, FFFFBCFB, DFCFFCFB, DFCFBFFF, D7DB9FFF, D7DBFDB9, D7BDFBD9, FFFF07E0, 007E0FFF,
03bdf020, 03def820, 08002300;
code：address start from 00000000
data：start address should be assigned

## Slide 19: U4-bus interface：MIO_BUS
MIO_BUS
  Module for CPU to exchange data with external
  This lab combine all data exchange circuit into one module
    simple，but not standard，hard for extension
    Will use standard bus in follow-up courses
      Wishbone bus
Basic function
  Data storage、interface for Seg7、SW、BTN and LED
This lab use IP soft core -- U4
  Core file: MIO_BUS.ngc
  Interface file (empty)：MIO_BUS.v
  Symbol file：MIO_BUS.sym
note：if increase RAM capacity, address decoder should be modified

## Slide 20: IO interface empty file-MIO_BUS.v
module MIO_BUS( input wire clk, input wire rst,
input wire [3:0] BTN, input wire [15:0]SW,
input wire mem_w,
input wire [31:0] Cpu_data2bus, //data from CPU
input wire [31:0] addr_bus, //addr from CPU
input wire [31:0] ram_data_out,
input wire [15:0] led_out,
input wire [31:0] counter_out,
input wire counter0_out,
input wire counter1_out,
input wire counter2_out,
output wire [31:0] Cpu_data4bus, //write to CPU
output wire [31:0] ram_data_in, //from CPU write to Memory
output wire [9: 0] ram_addr, //Memory Address signals
output wire data_ram_we,
output wire GPIOf0000000_w, // GPIOffffff00_we
output wire GPIOe0000000_we, // GPIOfffffe00_we
output wire counter_we, //记数器
output wire [31:0] Peripheral_in //送外部设备总线
);
endmodule

## Slide 21: Signals of MIO_BUS
MIO_BUS U4( clk_100HzM, //clock on board
rst, //reset，button BTN3
BTN [3:0] , //4 bits original button input
SW [15:0], //8 bits original switch input
mem_w, //memory read/write signal，from CPU
Cpu_data2bus [31:0] , //CPU data output bus
addr_bus [31:0] , //address bus，from CPU
ram_data_out [31:0] , //from RAM data output
led_out [7:0], //from LED output
counter_out [31:0] , //当前通道计数输出，来自计数器外设
counter0_out, //通道0计数结束输出，来自计数器外设
counter1_out, //通道1计数结束输出，来自计数器外设
counter2_out, //通道2计数结束输出，来自计数器外设
Cpu_data4bus [31:0] , //CPU写入数据总线，连接到 CPU
ram_data_in [31:0] , //RAM 写入数据总线，连接到RAM
ram_addr [9: 0] , //RAM访问地址，连接到RAM
data_ram_we, //RAM读写控制， 连接到RAM
GPIOf0000000_w, // 设备一LED写信号
GPIOe0000000_we, // 设备二7段写信号，连接到U5
counter_we, //记数器写信号，连接到U10
Peripheral_in [31:0] //外部设备写数据总线，连接所有写设备
);
endmodule

## Slide 22
GPIO interface module
--same with lab 3

## Slide 23: U7-GPIO device interface 1-- SPIO
Device GPIO
& LED
clk_io
GPIOf0000000_we
Peripheral_in
8-LED
led_out
Counter_set
GPIOf0
rst
22位
GPIO output device
  address=f0000000 - ffffffff0 (ffffff00-ffffffff0)
  Read/write control signal：GPIOf0000000_we(GPIOffffff00_we)
  {GPIOf0[21:0],LED,counter_set}
Function
  LEDs and counter 控制器读写
  可回读，检测状态
In this lab, we use soft IP core- U7
  Core calling: SPIO.ngc
  interface file：SPIO_IO.v
  symbol：SPIO.sym

## Slide 24: IP core call empty module -PIO.v
  module PIO(input clk, //io_clk，与CPU反向
  input rst,
  input EN, //来自U4
  input [31:0] P_Data, //来自U4
  input Start //串行输出启动
  output [1:0] counter_set, //来自U7，后继用
  output [15:0] led_out, //输出到LED,回读到U4
  output [13:0] GPIOf0 //备用
  output led_clk, //串行时钟
  output led_sout, //串行LEDE值
  output LED_PED, //LED使能
  output led_clrn //LED清零
  );
  endmodule

## Slide 25: U6-GPIO device 2: SSeg_Dev
7-seg display module
  Connect to CPU through Multi_8CH32
  address=E0000000 - EFFFFFFF (FFFFFE00-FFFFFEFF)
Function (refer to lab2)
Use soft IP core - U5
  SSeg7_Dev.ngc
  SSeg7_Dev.v
  SSeg7_Dev.sym

## Slide 26: U6-GPIO device 2： Seg7_Dev
7-seg display module
  Connect to CPU through Multi_8CH32
  address=E0000000 - EFFFFFFF (FFFFFE00-FFFFFEFF)
Function (refer to lab2)
Use soft IP core - U5
  SSeg7_Dev.ngc
  SSeg7_Dev.v
  SSeg7_Dev.sym
SP3 is compatible with adurino

## Slide 27: Interface file: SSeg7_Dev.v
  module SSeg7_Dev(input wire [31:0] disp_num, //来自U5
  input wire [1:0]SW, //来自U9
  input wire flash_clk, //通用分频器
  input wire [1:0] Scanning, //来自U8
  input wire [3:0] pointing, //来自U5
  input wire [3:0] blinking, //来自U5
  output wire [3:0] AN,
  output reg [7:0] SEGMENT //来自U5
  );
  endmodule

## Slide 28: U5- Interface module Multi_8CH32
GPIO
Multi_8CH32
clk_io
GPIOe0000000_we
Peripheral_in
Seg7 Device
disp_num
rst
…
Test_data0
Test_data7
…
Peripheral_in
GPIO output interface module
  address=E0000000 - EFFFFFFF (FFFFFE00-FFFFFEFF)
  Read/write control signal：GPIOe0000000_we(GPIOfffffe00_we)
Function (refer to Exp02)
  Data0 as the display interface
    GPIOe0000000_we=1
    CLK positive edge
  Data1-data7: debug signal
Use soft IP core U6
  核调用模块Multi_8CH32.ngc
  核接口信号模块(空文档)： Multi_8CH32_IO.v
  核模块符号文档：Multi_8CH32.sym

## Slide 29: Interface file -Multi_8CH32_IO.v
  module Multi_8CH32 ( input clk, //io_clk，同步CPU
  input rst,
  input EN, //=1, 通道0显示
  input[63:0]point_in, //针对8个显示通道各8个小数点
  input[63:0]blink_in, //针对8个通道各8位闪烁控制
  input [2:0] Test, //通道选择SW[7:5]
  input [31:0] Data0, //通道0
  input [31:0] data0, //通道1
  input [31:0] data1, //通道2
  input [31:0] data2, //通道3
  input [31:0] data3, //通道4
  input [31:0] data4, //通道5
  input [31:0] data5, //通道6
  input [31:0] data6, //通道7
  output reg[3:0] point_out, //小数点输出
  output reg[3:0] blink_out, //闪烁控制输出
  output [31:0] disp_num //接入7段显示器
  );
  endmodule

## Slide 30: Signals of Multi_8CH32
  Multi_8CH32 U5( .clk(clk_io), .rst(rst),
  . EN(GPIOe0000000_we), //来自U4
  . point_in(point_in), //外部输入
  .blink_in(blink_in), //外部输入
  .Test(SW_OK[7:5]), //来自U9
  .Data0(Peripheral_in), //来自U4
  .data1({2‘b00,PC_out[31:2]}), //来自U1
  .data2(counter_out), //来自U10
  .data3(Inst), //Inst，来自CPU
  .data4(addr_bus), //来自CPU
  .data5(Cpu_data2bus), //来自CPU
  .data6(Cpu_data4bus), //来自CPU
  .data7(PC_out), //来自CPU;
  .point_out(point_out), //输出到U6
  .blink_out(blink_out), //输出到U6
  .disp_num(disp_num) //输出到U6
  );

## Slide 31: GPIO device interface 3,4: Device_GPIO_SW_BTN
8-bits Switch and 4-bits Button input
  address= f0000000-ffffffff0，A[2]=0
  These two devices are included in U4，MIO_BUS
  Relation with CPU data bus（when addre_bus=f0000000）
Cpu_data4bus = {counter0_out, counter1_out, counter2_out, 1'h000, BTN,SW};
CPU
clk_io
Cpu_data4bus
addre_bus=f0000000
Led out
BTN
SW
mem_w=0

## Slide 32: U10-peripheral device 5: Counter_x.v
General counter，
  address=F0000004 – FFFFFFF4 (FFFFFF04-FFFFFFF4)
  r/w control：counter_we
Function
  3 paths independent counter
  Output for choose path or initialization
    counter_set=00、01、10 for path0、1、2
    counter_set=11对应计数通道工作设置
Use soft IP core- U10
  核调用模块Counter_x.ngc
  核接口信号模块(空文档)：Counter_x.v
  核模块符号文档：Counter_x.sym

## Slide 33: Interface file -Counter_x.v
module Counter_x(input clk, //io_clk
input rst,
input clk0, //clk_div[7]，来自U8
input clk1, // clk_div[10]，来自U8
input clk2, //clk_div[10]，来自U8
input counter_we, //计数器写控制，来自U4
input [31:0] counter_val, //计数器输入数据，来自U4
input [1:0] counter_ch, //计数器通道控制，来自U7
output counter0_OUT, //输出到U4
output counter1_OUT, //输出到U4
output counter2_OUT, //输出到U4
output [31:0] counter_out //输出到U4
);
endmodule

## Slide 34
SOC auxiliary modules
U8：clk_div
U9：anti-jitter
Refer to previous lab

## Slide 35: clk_div.v
module clk_div(input clk,
input rst,
input SW2,
output [31:0]clkdiv,
output Clk_CPU
);
endmodule

## Slide 36: Anti_jitter.v
  module SAnti_jitter(input clk, //主板时钟
  input RSTN
  input readn //阵列式键盘读
  input [3:0]Key_y, //阵列式键盘列输入
  output reg[4:0] Key_x, //阵列式键盘行输出
  output reg[4:0] Key_out,//阵列式键盘扫描码
  output reg Key_ready, //阵列式键盘有效
  input [15:0] SW, //开关输入
  output reg [3:0] ] BTN_OK,//列按键输出
  output reg [3:0] pulse, //列按键脉冲输出
  output reg [15:0] SW_OK, //开关输出
  output reg CR, //RSTN短按输出
  output reg rst //复位， RSTN长按输出
  );
  endmodule

## Slide 37: Multi_8CH32 signals
  Multi_8CH32 U5( .clk(clk_io), .rst(rst),
  . EN(GPIOe0000000_we), //来自U4
  . point_in(point_in), //外部输入
  .blink_in(LE_in), //外部输入
  .Test(SW_OK[7:5]), //来自U9
  .Data0(Peripheral_in), //来自U4
  .data1({2‘b00,PC_out[31:2]}), //来自U1
  .data2(counter_out), //来自U10
  .data3(Inst), //Inst，来自CPU
  .data4(addr_bus), //来自CPU
  .data5(Cpu_data2bus), //来自CPU
  .data6(Cpu_data4bus), //来自CPU
  .data7(PC_out), //来自CPU;
  .point_out(point_out), //输出到U6
  .LE_out(blink_out), //输出到U6
  .disp_num(disp_num) //输出到U6
  );

## Slide 38: Course Outline
Environment
Task
Principle
Implementation

## Slide 39: Project：OExp09-IP2MCPU
Build CPU debugging、testing environment
  Top implemented in HDL，call IP core modules
    Module name：Top_OExp09_IP2MCPU.sch
Use SOC integration to implement testing framework
  Reuse modules of lab 3 except SCPU
    CPU (given IP core)：U1
    RAM (ISE build IP core)：U3
    BUS(given IP core)：U4
    8-to-1 datapath(Multi_8CH32 of lab1)：U5
    7-seg display(SSeg7_Dev IP of lab2)：U6
    LED display(SPIO of lab2)：U7
    通用分频模块(clk_div)：U8
    开关去抖模块(IP core)：U9
    Data input (IP core)：M4(not in use for the moment)
Decompose CPU into two IP cores
  After SOC debugging, use two IP cores to build MCPU

## Slide 40: Design
Build multicycle SOC testing environment
--new project OExp09-IP2MCPU

## Slide 41: Build multicycle SOC environment
New SOC testing project in ISE
  Reference project name：ORG-Exp09或OExp09_IP2MCPU
This project is shared for multicycle CPU design
HDL
Top-level Source type

## Slide 42: Project interface

## Slide 43
Copy U1、U3~U10、multicycle controller、datapath soft core(.ngc) files to current project dir
--except your own implemented modules
--better use your own clk_div
This lab use HDL description, don’t need to copy module symbol files

## Slide 44: Design multicycle CPU module
Use HDL to call IP core and implement CPU
  Suggested name：Multi_CPU.v或MCPU.v

## Slide 45: CPU HDL description reference
module Muliti_CPU(input clk, //muliti_CPU
input reset,
input MIO_ready,
output[31:0] PC_out, //TEST
output[31:0] inst_out, //TEST
output mem_w,
output[31:0] Addr_out,
output[31:0] Data_out,
input [31:0] Data_in,
output CPU_MIO,
input INT,
output[4:0]state //Test
);
endmodule
………… variable statement：attention signal width for all wire statements
…………initialization、temp signal，bus transition etc
………… module call：2 calls

## Slide 46: Key signals and module calls
……
assign mem_w=MemWrite&&(~MemRead);
assign PC_out=PC_Current;
ctrl x_ctrl(.clk(clk),
.reset(reset),
.Inst_in(inst_out),
……
.PCWrite(PCWrite),
.PCWriteCond(PCWriteCond),
.Branch(Branch)
);
M_datapath x_datapath(.clk(clk),
.reset(reset),
.MIO_ready(MIO_ready),
……
.M_addr(Addr_out),
.zero(zero),
.overflow(overflow)
);

## Slide 47
SOC framework top description
--HDL，call IP core module

## Slide 48: According to the following schematic to write HDL code simple：just interface definition and module call

## Slide 49: Build top module
New top module
  Default dir is project dir “Exp09_IP2MCPU”
  Suggested to change as “Exp09_IP2CPU \Code”
note：put all codes into a separate directory for convenience ！
  Note conflicts for the same name .sch and .v files
Write top code according to schematic fig
  Use SOCMF.v as an example

## Slide 50
代码输入区

## Slide 51: The second level
CPU核

## Slide 52: Syntax checking for top
Checking signal connection
  Active Design window
  Choose top：SOCMF.v
  In the running window： choose Synthesze→Check Syntax
  Note
    It won’t check logic function
    Only code syntax
    Pay attention to bus connection
      Real Connection
      Name/rename

## Slide 53: Module call and connection
method
  Module_name call_number(port signal list)；
  Port signal corresponds to:
    Signals in the module
    Refered use brancket：.signal in the module(input)
    eg：.clk(clk_100mHz)
Relation of called modules
  Put module Symbol in top module, the corresponding modules will be called directly
  Connect the interface module and soft core module
    Contains only the interface signal, there is no code inside.v
      Synthesizer will connect the signals
  Click “Add Source” to connect the corresponding empty module b

## Slide 54: Top (SOC test environment) reference
module IP2CPU(input clk_50mhz,
input [3:0]BTN,
input [7:0]SW,
output[7:0]LED,
output[7:0]SEGMENT,
output[3:0]AN_SEL
);
Wire Clk_CPU, rst, clk_m, mem_w, data_ram_we, GPIOf0000000_we, GPIOe0000000_we, counter_we;
wire counter_OUT0, counter_OUT1, counter_OUT2;
wire [1:0]Counter_set;
wire MIO_ready;
wire CPU_MIO;
endmodule
………… module calls ：9 modules
………… variable statement：attention signal width for all wire statements
…………initialization、temp signal，bus transition etc

## Slide 55: Signal transmission： initialization、temp signal when connecting modules，signal transformation、bus transformation
assign MIO_ready=~button_out[1]; //CPU永远不等待，或=1
assign SW2=SW_OK[2]; //信号传输
assign LED={led_out[7]|Clk_CPU,led_out[6:0]};//总线转换
assign clk_m=~clk_50mhz;
…………
assign clk_io=~Clk_CPU;
…………

## Slide 56: Module calls
  SAnti_jitter U9(clk, //主板时钟
  RSTN
  readn
  Key_y, //阵列式键盘列输入
  Key_x, //阵列式键盘行输出
  Key_out, //阵列式键盘扫描码
  ……
  rst //复位， RSTN长按输出
  );
clk_div U8(clk_50mhz, // Clock divider-时钟分频器
rst,
SW2,
clkdiv,
Clk_CPU
);

## Slide 57: Module calls
SSeg7_Dev U6( .disp_num(disp_num),
. SW(SW_OK(1:0)),
……
……
.AN(digit_anode)
);
Muliti_CPU U1(.clk(Clk_CPU),
.reset(rst),
.MIO_ready(MIO_ready), //MIO_ready
……
……
.state(state) //Test
);
Notes:   (input wire [31:0] disp_num, //来自U5
  input wire [1:0]SW, //来自U9
  input wire flash_clk,

## Slide 58: Module calls
RAM_B U3(.clka(clk_m),
.wea(data_ram_we),
.addra(ram_addr), // Addre_Bus [9 : 0]
.dina(ram_data_in),
.douta(ram_data_out) //Data_Bus [31 : 0]
);
MIO_BUS U4( .clk(clk_50mhz),
……
……
.Peripheral_in(Peripheral_in)
);

## Slide 59: Module calls
led_Dev_IO U7( clk_io,
……
……
GPIOf0 );
seven_seg_Dev_IO U5( .clk(??),
.rst(rst),
.GPIOe0000000_we(??),
.Test(SW_OK[7:5]),
.disp_cpudata(??), //CPU data output
.Test_data1({2'b00,pc[31:2]}), //pc[31:2]
.Test_data2(counter_out), //counter
.Test_data3(??), //Inst
.Test_data4(??), //addr_bus
.Test_data5(??), //Cpu_data2bus;
.Test_data6(??), //Cpu_data4bus;
.Test_data6(??), //pc; .disp_num(??)
);

## Slide 60: Module calls
Counter_x U10(.clk(clk_io),
.clk0(clkdiv[9]),
.clk1(clkdiv[10]),
.clk2(clkdiv[10]),
.counter_we(counter_we),
.counter_val(Peripheral_in),
.counter_ch(Counter_set),
.counter0_OUT(counter_OUT0),
.counter1_OUT(counter_OUT1),
.counter2_OUT(counter_OUT2),
.counter_out(counter_out)
);
endmodule

## Slide 61: Finished module relations
Top use HDL description
IP core integrated CPU
Either HDL or schematic to describe CPU

## Slide 62
SoC physical verification
-no test for this lab，just use DEMO to verify functions
-same as lab3, lab4

## Slide 63: DEMO interface
SW[7:5]=显示通道选择
SW[7:5]=000：CPU程序运行输出
SW[7:5]=001：测试PC字地址
SW[7:5]=010：测试指令字
SW[7:5]=011：测试计数器
SW[7:5]=100：测试RAM地址
SW[7:5]=101：测试CPU数据输出
SW[7:5]=110：测试CPU数据输入
SW[0]=文本图形选择
SW[1]=高低16位选择
SW[2]=CPU单步时钟选择
SW[4:3]=00，点阵显示程序：跑马灯
SW[4:3]=00，点阵显示程序：矩形变幻
SW[4:3]=01，内存数据显示程序：0～F
SW[4:3]=10，当前寄存器+1显示
W15 SW14 SW13 SW12 SW11 SW10 SW9 SW8 SW7 SW6 SW5 SW4 SW3 SW2 SW1 SW0
LED15 LED14 LED13 LED12 LED11 LED10 LED9 LED8 LED7 LED6 LED5 LED4 LED3 LED2 LED1 LED0
X0Y3
X0Y2
X0Y1
X0Y0
X1Y3
X1Y2
X1Y1
X1Y0
X2Y3
X2Y2
X2Y1
X2Y0
X3Y3
X3Y2
X3Y1
X3Y0
X4Y3
X4Y2
X4Y1
X4Y0
MCU3
PRGO
RSTN
MCU1~2
Ardunio
SEG0
SEG1
SEG2
SEG3
SEG0
SEG1
SEG2
SEG3
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
没有使用

## Slide 64: Download and test SoC
Simulation without IP core
  Do simulation for your owned designed module(pass those that have been simulated in single-cycle labs)
  No simulation for the given IP core
SOC physical verification
  Download .bit file
  test functions of SOC
    Debugging if there is any error
  qualitatively observe key signals of SOC
    use mem.coe as test code and test data*

## Slide 65: Switch test
Graphical function test
Text function test
开关 | 位置 | 功能
SW[1:0] | X0 | 七段码图形显示
SW[2] | 0 | CPU全速时钟
SW[4:3] SW[4:3] | 00 11 | 7段码从上至下亮点循环右移 7段码矩形从下到大循环显示
SW[7:5] | 000 | 作为外设使用（E0000000/FFFFFE00）
开关 | 位置 | 功能
SW[1:0] | 01 11 | 七段码文本显示（低16位） 七段码文本显示（高16位）
SW[2] | 0 | CPU全速时钟
SW[4:3] SW[4:3] | 01 10 | 7段码显示RAM数字 7段码显示累加
SW[7:5] | 000 | 作为外设使用（E0000000/FFFFFE00）

## Slide 66: Qualitatively observation
SOC signal testing
  CPU running in one step
  Switch test
开关 | 位置 | 功能
SW[1:0] | 01 | 七段码文本显示（低16位）
SW[1:0] | 11 | 七段码文本显示（高16位）
SW[2] | 0 | CPU全速时钟
SW[7:5] | 010 | Counter值输出
SW[7:5] | 100 | CPU数据存储地址addr_bus（ALU）
SW[7:5] | 101 | CPU数据输出Cpu_data2bus (寄存器B)
SW[7:5] | 110 | CPU数据输入Cpu_data4bus(RAM输出)

## Slide 67: Qualitatively observation
SOC signal testing
  CPU running step by step
  Switch testing
  Design test program to substitute DEMO*
开关 | 位置 | 功能
SW[1:0] | 01 | 七段码文本显示（低16位）
SW[1:0] | 11 | 七段码文本显示（高16位）
SW[2] | 1 | CPU单步时钟
SW[7:5] | 001 | CPU指令字地址PC_out[31:2]
SW[7:5] | 011 | ROM指令输出Inst_in
SW[7:5] | 100 | CPU数据存储地址addr_bus(ALU输出)
SW[7:5] | 101 | CPU数据输出Cpu_data2bus(寄存器B)
SW[7:5] | 110 | CPU数据输入Cpu_data4bus(RAM输出)
SW[7:5] | 111 | CPU指令字节地址PC_out

## Slide 68
END