## Slide 1: Computer Organization & Design The Hardware/Software Interface
刘海风
Asso. Prof. Haifeng Liu
College of Computer Science and Technology, Zhejiang University
haifengliu@zju.edu.cn
计算机组成与设计
Chapter 2
Instructions ：Language of the Machine

## Slide 2: MIPS vs. ARM
Category | MIPS | ARM
Arithmetic | ADD $r1, $r2, $r3 | ADD r1, r2, r3
 | SUB $r1, $r2, $r3 | SUB r1, r2, r3
Data Transfer | LW $r1, 100($r2) | LDR r1, [r2, #100]
 | SW $r1, 100($r2) | SDR r1, [r2, #100]
 | LH $r1, 100($r2) | LDRH r1, [r2, #100]
 | SH $r1, 100($r2) | SDRH r1, [r2, #100]
Logical | AND $r1, $r2, $r3 | AND r1, r2, r3
 | SLL $r1, $r2, 10 | LSL r1, r2, #10
Conditional branch | SLT $r1, $r2, $r3 | CMP r1, r2
 | Beq $r1, $r2, Lable | BEQ Lable
 | Bne | 
Unconditional branch | J Lable | B Label
 | JAL Lable | BL Label
 | JR $ra | Mov PC LR

## Slide 3: Contents of Chapter 2
2.1 Introduction
2.2 Operations of the Computer Hardware
2.3 Operands of the Computer Hardware
2.4 Representing Instructions in the Computer
2.5 Logical Operation
2.6 Instructions for Making Decisions
2.7 Supporting Procedures in Computer Hardware
2.8 Communicating with People
2.9 MIPS Addressing for 32 Bit Immediates and Addresses

## Slide 4
2.10 Translanting and starting a Program
2.11 *How Compilers Optimize
2.12 *How Compilers Work
2.13 A C Sort Example to Put It All together
2.14 *Implementing an Object-Oriented Language
2.15 Arrays Versus Pointers
2.16 Real Stuff: IA-32 Instructions
2.17 Fallacies and Pitfalls
2.18 Concluding Remarks
2.19 Historical Perspective and Further Reading

## Slide 5: Introduction
Language of the machine
  Instructions → Statement
  Instruction set → Syntax
Design goals
  Maximize performance
  Minimize cost
  Reduce design time
Our chosen instruction set: MIPS
  Similar to other ones developed since the 1980's
  Used by NEC, Nintendo, Silicon Graphics, Sony

## Slide 6: Instruction characteristics
Type of internal storage in processer
The number of the memory operand in the instruction
Operations in the instruction Set
Type and Size of Operands
Representing Instructions in the Computer
  Encoding
Op
Operands
wide variety
Operators

## Slide 7: Type of internal storage in processer
Stack
Accumulator
General purpose register
  Register-Memory
  Register-Register：load/store

## Slide 8: The number of the memory operand In the instruction
Register-Register
  Maximum number of operands allowed 3
  Number of memory addresses is 0
Register-memory
  Maximum number of operands allowed 2
  Number of memory addresses is 1
Memory-memory
  Maximum number of operands allowed 2 or 3
  Number of memory addresses is 2 or 3

## Slide 9: Variables difference
C
  Int char f
Instruction Set
  Register
  Memory address
    Displacement
    Immediate
  Stack

## Slide 10: 2.2 Operations of the Computer Hardware
Every computer must be able to perform arithmetic
  Only one operation per instruction
  Exactly three variables add a,b,c a←b+c
Design Principle 1
  Simplicity favors regularity
Example 2.1
Compiling two simple C statements
  C code:
  a = b + c;
  d = a – e;
  MIPS code:
  add a, b, c
  sub d, a, e

## Slide 11: Arithmetic
Example 2.2 Compiling a complex C statement
  C code:
  f = ( g + h ) – ( i + j );
  MIPS code:
  add t0, g, h # temporary variable t0 contains g + h
  add t1, i, j # temporary variable t1 contains i + j
  sub f, t0, t1 # f gets t0 – t1
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add a,b,c | a←b+c | Always three operand
 | subtract | sub a,b,c | a←b-c | Always three operand
  MPIS assembly language

## Slide 12: 2.3 Operands of the Computer Hardware
Register Operands
Memory Operands
Constant or Immediate Operands

## Slide 13: Register Operands
Register Operands
  Arithmetic instructions operands must be registers
  Difference between the variables of a programming
    Registers is limited number of
      32 registers in MIPS
      32 bits for each register in MIPS
Design Principle 2
  Smaller is faster
MIPS convention for registers
  $s0, $s1, … for registers corresponding to variables in C
  $t0, $t1, … for temporary registers for compiler
and Java

## Slide 14: Operate with Register Operands
Example 2.3 Compiling a C statement using registers
  C code
  f = ( g + h ) – ( i + j ) ;
  MIPS code
  add $t0, $s1, $s2 # $t0 contains g + h
  add $t1, $s3, $s4 # $t1 contains i + j
  sub $s0, $t0, $t1 # f gets $t0 - $t1

## Slide 15: Memory Operands
Advantage
  Could save much more data
  Save complex data structures
    Arrays and structures
Data transfer instructions
  Load: from memory to register; load word ( lw )
  Store: from register to memory; store word( sw )
Memory addresses and contents at those locations
1
0
0
1
0
1
0
1
1
3
2
1
0
D
a
t
a
Address
Memory
Processor

## Slide 16
Example 2.4 Compiling with an operand in memory
C code:
  g = h + A[8] ; // A is an array of 100 words ( Assume: g ---- $s1 h ---- $s2 base address of A ---- $s3 )
  MIPS code:
  lw $t0, 8($s3) # temporary reg $t0 gets A[8]
  add $s1, $s2, $ t0 # g = h + A[8]
  Offset: the constant in a data transfer instruction →8($s3)
  Base register: the register added to form the address
Byte addressing
  →8($s3)
Alignment restriction
  Addresses of words are multiples of 4 in MIPS
→32($s3)

## Slide 17: Software/hardware interface
Compiler allocates data structures to memory Compiler associating variables with registers
Actual MIPS memory addresses and contents
1
0
0
1
0
1
0
1
1
C
8
4
0
Data
Address
Memory
Processor
Registers
The offset to be added to $s3 in Example 2.4 must be 4×8

## Slide 18: Memory Alignment
18
struct {
int a;
char b;
char c[2];
char d[3]
float e;
}
a
b
e
No use
No use
No use
C[0]
C[1]
No use
No use
D[0]
d[1]
D[2]
No use
D[0]
d[1]
D[2]
e
e
No use
错误
因为内存一次只能读出4字节内存中的一行
这样布局，e变量不能一次读出

## Slide 19
Example 2.5 Compiling using load and store
  C code:
  A[12] = h + A[8] ; // A is an array of 100 words ( Assume: h ---- $s2 base address of A ---- $s3 )
  MIPS code:
  lw $t0 , 32($s3) # temporary reg $t0 gets A[8]
  add $t0, $s2, $ t0 # temporary reg $t0 gets h + A[8]
  sw $t0, 48($s3) # stores h + A[8] back into A[12]

## Slide 20: Discussion：How to represent?
g = h + A[i]
( Assume: g, h, i -- $s1, $s2, $s4 base address of A -- $s3 )

## Slide 21: g = h + A[i]
Example 2.6 Compiling using a variable array index
  C code:
  g = h + A[i] ; // A is an array of 100 words ( Assume: g, h, i -- $s1, $s2, $s4 base address of A -- $s3 )
  MIPS code:
  add $t1, $s4, $s4 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s3 # $t1 = address of A[i] (4 * i + $s3)
  lw $t0 , 0($t1) # temp reg $t0 = A[i]
  add $s1, $s2, $t0 # g = h + A[i]
Spilling registers Putting less commonly used variables(or those needed later)
into memory

## Slide 22: Discussion：How to represent?
Constant
  Many time a program
  will use a constant in an operation
g = h + 55

## Slide 23
Constant or immediate Operands
  Many time a program will use a constant in an operation
    Incrementing index to point to next element of array
    Add the constant 4 to register $s3
    Assuming AddrConstants 55 is address pointer of constant 55
Prestored in memory
lw $t0, AddrConstant55($s1) # $t0=constant 55
add $s3, $s3, $t0 #$s3=$s3+$t0($t0==55)
55
….
$s1
AddrConstants 55

## Slide 24: Immediate Operands
Immediate Operands
  Avoids the load instruction
  Immediate: Other method for adding constant 55 to $s3
    Offer versions of the instruction
    addi $s3, $s3, 55 #$s3= $s3+ 55
  Short Literal
Design Principle 3
  Make the common case fast: (why?) Constant operands occur frequently it is very common Loading them from memory is very slow
  Short Literal
OP

## Slide 25: Brief summary
Name | Example | Comments
32 register | $s0,$s1…… $t0, $t1……. | Fast locations for data. In MIPS, data must be in registers to perform arithmetic.
230 memory words | Memory[0], Memory[4] , Memory[8], …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr. , so sequential word addr. Differ by 4. Memory holds data structures, arrays, and spilled registers.
MIPS operands
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
 | Add immediate | addi $s1,$s2,100 | $s1=$s2+100 | Used to add constants
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
MIPS assembly language
Notes: 是否需要立即数减？

## Slide 26: 2.4 Representing Instructions in the Computer --Instruction Format
All information in computer consists of binary bits
Mapping registers into numbers(index)
  Map registers $s0 to $s7 onto registers 16 to 23
  Map registers $t0 to $t7 onto registers 8 to 15
Example 2.7 Translating assembly into machine instruction
  MIPS code
  add $t0, $s1, $s2
  Decimal version of machine code
  | 0 | 17 | 18 | 8 | 0 | 32 |
  Binary version of machine code
  | 000000 | 10001 | 10010 | 01000 | 00000 | 100000 |
  6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Sometime use Hex!

## Slide 27: MIPS fields (format)
op：basic operation of the instruction, traditionally called the opcode.
rs： the first register source operand.
rt： the second register source operand.
rd： the register destination operand.
shamt： shift amount.
funct： function,this field selects the specific variant of the operation in the op field.
Must bear in mind !
Field size | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | op | rs | rt | Imm/address |  |  | Data transfer ,branch format
J-format | op | target address (word) |  |  |  |  | Uncondition-al jump
Region: ±215

## Slide 28
Design Principle 3
  Good design demands good compromises
All instructions in MIPS have the same length
  Conflict: same length ← → single instruction

## Slide 29: I-format example
Example:
  MIPS code: lw $t0, 32($s3)
  Decimal version of machine code
  | 35 | 19 | 8 | 32 |
  Binary version of machine code
  | 100011 | 10011 | 01000 | 100000 |
  6 bits 5 bits 5 bits 16 bits
R-format and I-format

## Slide 30
Example 2.8 Translating assembly into machine instruction
C code:
  A[300] = h + A[300] ; ( Assume: h ---- $s2 base address of A ---- $t1 )
  MIPS assembly code:
  lw $t0, 1200($t1) # temporary reg $t0 gets A[300]
  add $t0, $s2, $t0 # temporary reg $t0 gets h + A[300]
  sw $t0, 1200($t1) # stores h + A[300] back into A[300]
  MIPS machine language code:
    Decimal version address/
    op rs rt rd shamt funct
  | 35 | 9 | 8 | 1200 |
  | 0 | 18 | 8 | 8 | 0 | 32 |
  | 43 | 9 | 8 | 1200 |
lw
add
sw

## Slide 31
    Binary version
  | 100011 | 01001 | 01000 | *0000 0100 1011 0000 |
  | 000000 | 10010 | 01000 | 01000 | 00000 | 100000 |
  | 101011 | 01001 | 01000 | 0000 0100 1011 0000 |
  Note the only difference of the first and last instructions!
Two key principles of today’s computers
  Instructions are represented as numbers
  Programs can be stored in memory like numbers
Store-program
lw
add
sw

## Slide 32: Stored-program concept

## Slide 33: 任务管理器
Ctrl+alt+del
  只能被MS截获
列出所有正在运行的任务
  任务的内存大小
  任务的CPU占有率
  任务的CPU时间
  PID为进程号
    越大越晚启动

## Slide 34: Trojan 最简单例子-密码窃取
main() {
char password[256], crypt_pw[256];
scanf(“%s”,password);
crypt(password, crypt_pw);
if ( strcmp(crypt_pw, “xxxxxx”)!=0 )
printf(“password error\n”);
else
;
}
Input: 123456
Trojan read memory variable “password”
123456
abcdef
a.exe
trojan
password
Crypt_pw

## Slide 35
000000 | 01000 | 10010 | 01000 | 00000 | 100000
op rs rt rd shamt funct
add $t0, $t0 , $s2,
00000001000100100100000000100000
Memory addr: 0x40000008
main() {
int *p;
p=0x40000008;
*p+=2
}
000000 | 01000 | 10010 | 01000 | 00000 | 100010
sub $t0, $t0 , $s2
问题：如果这是一个执行程序拳击游戏，该行指令表示您挨打，血(t0)在减少(s2为负数)，当血小于等于0，KO。
用ultraedit将该二进制执行文件修改，让自己不损血，怎么改？

## Slide 36: Demo:Edit the execute file and memory
Change the program info(static)
  Use hex edit tools
  Eg:use ultraedit, change title
    Leapftp -> leepftp
Change the program info(run time)
  Use memory edit tools
  Eg:use 金山游侠, change data

## Slide 37: 脱壳shell
一个执行程序，有判断是否为盗版，问如何crack
查找判断之处，找到后看变量作用位置
找到惩罚处，将该处的二进制代码改成noop
main() {
int expired=false;
calculate expired；
if (expired) {
printf(“软件过期了\n”);
exit(1); -> “;” -> noop
}
else ..
}

## Slide 38: MIPS operands, assembly and machine language
Name | Format | Example |  |  |  |  |  | Comment
add | R | 0 | 18 | 19 | 17 | 0 | 32 | add $s1, $s2, $s3
sub | R | 0 | 18 | 19 | 17 | 0 | 34 | sub $s1, $s2, $s3
addi | I | 8 | 18 | 17 | 100 |  |  | addi $s1,$s2,100
lw | I | 35 | 18 | 17 | 100 |  |  | lw $s1, 100($s2)
sw | I | 43 | 18 | 17 | 100 |  |  | sw $s1, 100($s2)
Field size |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | R | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
I-format | I | op | rs | rt | address |  |  | Data transfer ,branch format
Name | Example | Comments
32 register | $s0,$s1……,$s7 $t0, $t1…….,$t7 | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. Registers $s0-$s7 map to 16-23 and $t0-$t7 map to 8-15.
230 memory words | Memory[0], Memory[4], Memory[8], …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr., so sequential word addr. Differ by 4. Memory holds data structures,arrays, and spilled registers.
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
 | Add immediate | addi $s1,$s2,100 | $s1=$s2+100 | Used to add constants
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory

## Slide 39: 2.5 Logical Operation
Operating some bits within word or individual bit
Logic operations | C operators | Java operators | MIPS instructions
Shift left | 〈〈 | 〈〈 | sll
Shift right | 〉〉 | 〉〉〉 | srl
Bit-by-bit AND | & | & | And, andi
Bit-by-bit OR | ¦ | ¦ | Or, ori
Bit-by-bit NOT | ~ | ~ | nor

## Slide 40
Shift operator
  Move all the bits in a word to left or right, filling emptied bits with 0
  Shifting left by i is same result as multiplying by 2i
  0000 0000 0000 0000 0000 0000 0000 1001 (9)10
  Shift left 4
  0000 0000 0000 0000 0000 0000 1001 0000 (9×16=144)10
  sll $t2, $s0, 4 #reg $t2=reg $s0<<4 bit
op | rs | rt | rd | shamt | funct
0 | 0 | 16 | 10 | 4 | 0

## Slide 41
AND operator
  It is bit-by-bit
    Result=1 : both bits of the operands are 1
  $t2:
  0000 0000 0000 0000 0000 1101 0000 0000
  $t1:
  0000 0000 0000 0000 0011 1100 0000 0000
  and $t0, $t1, $t2 #reg $t0=reg $t1 & reg $t2
  Result:
  0000 0000 0000 0000 0000 1100 0000 0000

## Slide 42
OR operator
  It is bit-by-bit
    Result=1 : either bits of the operands is 1
  $t2:
  0000 0000 0000 0000 0000 1101 0000 0000
  $t1:
  0000 0000 0000 0000 0011 1100 0000 0000
  or $t0, $t1, $t2 #reg $t0=reg $t1 | reg $t2
  Result:
  0000 0000 0000 0000 0011 1101 0000 0000

## Slide 43
NOR operator
  NOT(A OR B)
    A NOR 0 =NOT(A OR 0)=NOT(A)
  $t1:
  0000 0000 0000 0000 0011 1100 0000 0000
  $t3:
  0000 0000 0000 0000 0000 0000 0000 0000
  nor $t0, $t1, $t3 #reg $t0=~(reg $t1 | reg $t3)
  Result:
  1111 1111 1111 1111 1100 0011 1111 1111

## Slide 44: MIPS operands
MIPS assembly language
Name | Example | Comments
32 register | $s0,$s1……,$s7 $t0, $t1…….,$t7 | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. Registers $s0-$s7 map to 16-23 and $t0-$t7 map to 8-15.
230 memory words | Memory[0],Memory[4] , Memory[8] , …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr., so sequential word addr. Differ by 4. Memory holds data structures,arrays, and spilled registers.
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | Add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | Sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
 | Add immediate | addi $s1,$s2,100 | $s1=$s2+100 | +constants; overflow detected
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
logical | and | and $s1,$s2,$s3 | $s1=$s2 & $s3 | three reg. operands;bit-by-bit AND
 | or | or $s1,$s2,$s3 | $s1=$s2 ¦ $s3 | three reg. operands;bit-by-bit OR
 | nor | nor $s1,$s2,$s3 | $s1=~($s2 ¦ $s3) | three reg. operands;bit-by-bit NOR
 | and immediate | addi $s1,$s2,100 | $s1=$s2 & 100 | Bit-by-bit AND reg with constant
 | or immediate | ori $s1,$s2,100 | $s1=$s2 ¦ 100 | Bit-by-bit OR reg with constant
 | shift left logical | sll $s1,$s2,10 | $s1=$s2 << 10 | Shift left by constant
 | shift right logical | srl $s1,$s2,10 | $s1=$s2 >> 10 | Shift right by constant

## Slide 45: 2.6 Instructions for making decisions
Branch instructions
  beq register1, register2, L1
  bne register1, register2, L1
Example 2.9 Compiling an if statement to a branch
( Assume: f ~ j ---- $s0 ~ $s4 )
  C code:
  if ( i = = j ) goto L1 ;
  f = g + h ;
  L1: f = f - i ;
  MIPS assembly code:
  beq $s3, $s4, L1 # go to L1 if i equals j
  add $s0, $s1, $s2 # f = g + h ( skipped if i equals j )
  L1: sub $s0, $s0, $s3 # f = f - i ( always executed )

## Slide 46
Example 2.10
Compiling if-then-else into Conditional Branches
( Assume: f ~ j ---- $s0 ~ $s4 )
  C code:
  if ( i = = j ) f = g + h ; else f = g - h ;
  MIPS assembly code:
  bne $s3, $s4, Else # go to Else if i ≠ j
  add $s0, $s1, $s2 # f = g + h ( Executed if i = = j if)
  j Exit # go to Exit
Else: sub $s0, $s1, $s2 # f = g - h ( Executed if i ≠ j else)
Exit: # the first instruction of the next C
…… statement
i==j?
f=g+h
f=g - h
Exit:
i==j
ij

## Slide 47
Example 2.11 Compiling a loop with variable array index
( Assume: g ~ j ---- $s1 ~ $s4 base of A[i] ---- $s5)
  C code:
  Loop: g = g + A[i] ; // A is an array of 100 words
  i = i + j ;
  if ( i != h ) goto Loop ;
  MIPS assembly code:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s5 # $t1 = address of A[i]
  lw $t0, 0($t1) # temp reg $t0 = A[i]
  add $s1, $s1, $t0 # g = g + A[i]
  add $s3, $s3, $s4 # i = i + j
  bne $s3, $s2, Loop # go to Loop if i != h
Supports LOOPs

## Slide 48
Example 2.12 Compiling a while loop
( Assume: i ~ k---- $s3 ~ $s5 base of save ---- $s6 )
  C code:
  while ( save[i] = = k )
  i = i + j ;
  MIPS assembly code:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s6 # $t1 = address of save[i]
  lw $t0, 0($t1) # temp reg $t0 = save[i]
  bne $t0, $s5, Exit # go to Exit if save[i] != k
  add $s3, $s3, $s4 # i = i + j
  j Loop # go to Loop
  Exit:

## Slide 49
set on less than -slt
  If the first reg. is less than second reg. then sets third reg to 1
  slt $t0, $s3, $s4 # $t0=1 if $s3 < $s4
Example 2.13 Compiling a less than test
( Assume: a -- $s0 b -- $s1 )
  C language:
  if (a < b), goto Less
  MIPS assembly code:
  slt $t0, $s0, $s1 # $t0 = 1 if $s0 < $s1 ( a < b)
  bne $t0, $zero, Less # go to Less if $t0 != 0 (that is, if a < b)
  ……
  Less:
Most popular Compare Operation
-- set on less than : slt

## Slide 50: For, do while, while
C code
For (i=0;i<100;i++）
  xxx（1行汇编）
MIPS code
ADD $R4, $R0, $R0
LOOP: SLT $R3, $R4, 100
BEQ $R3, $R0, exit
Xxx
ADD $R4, $R4, 1
J LOOP
Exit:
100次循环运行，运行时间=1+5*100+2
C code
i=0;
Do {
  xxx（1行汇编）
  i++;
  } while (i<100);
MIPS code
ADD $R4, $R0, $R0
LOOP: Xxx
Add $R4, $R4, 1
SLT $R3, $R4, 100
Bne $R3, $R0, LOOP
Exit:
100次循环运行，运行时间=1+4*100
C code
i=0;
while (i<100); {
  xxx（1行汇编）
  i++;
  }
MIPS code
ADD $R4, $R0, $R0
LOOP: SLT $R3, $R4, 100
BEQ $R3, $R0, exit
LOOP: Xxx
Add $R4, $R4, 1
J LOOP
Exit:
100次循环运行，运行时间=1+5*100+2
虽然直接从C翻译到汇编，性能有差距，然而通过编译技术可以实现相同的性能优化

## Slide 51
used to select one of many alternatives
Example 2.14
Compiling a switch using jump address table
( Assume: f ~ k ---- $s0 ~ $s5 $t2 contains 4 )
  C code:
  switch ( k ) {
  case 0 : f = i + j ; break ; /* k = 0 */
  case 1 : f = g + h ; break ; /* k = 1 */
  case 2 : f = g - h ; break ; /* k = 2 */
  case 3 : f = i - j ; break ; /* k = 3 */
  }
Hold out Case/Switch

## Slide 52: Jump register & jump address table
Jump with register content
jr $r
jump address table
K=0 | P1 address
K=1 | P2 address
K=2 | P3 address
K=3 | P4 address
$t4
 | …………
P1 address | Program 1
 | …………
P2 address | Program 2
 | …………
P3 address | Program 3
 | …………
P4 address | Program 3
 | …………
$r←$t4+4*K

## Slide 53
L0: add $s0, $s3, $s4 # k = 0 so f gets i + j
  j Exit # end of this case so go to Exit
L1: add $s0, $s1, $s2 # k = 1 so f gets g + h
  j Exit # end of this case so go to Exit
L2: sub $s0, $s1, $s2 # k = 2 so f gets g - h
  j Exit # end of this case so go to Exit
L3: sub $s0, $s3, $s4 # k = 3 so f gets i - j
  Exit: # end of switch statement
  MIPS assembly code:
  slt $t3, $s5, $zero # test if k < 0
  bne $t3, $zero, Exit # if k < 0, go to Exit
  slt $t3, $s5, $t2 # test if k < 4
  beq $t3, $zero, Exit # if k >= 4, go to Exit
  add $t1, $s5, $s5 # temp reg $t1 = 2 * k (0<=k<=3)
  add $t1, $t1, $t1 # temp reg $t1 = 4 * k
  add $t1, $t1, $t4 # $t1 = address of JumpTable[k]
  lw $t0, 0($t1) # temp reg $t0 = JumpTable[k]
  jr $t0 # jump based on register $t0
jump address table
$t1= $t4+4 * k:
L0:address
L1:address
L2: address
L3:address
Boundary
Memory1
Memory2

## Slide 54
Important conception--basic block
  A sequence of instructions without branches (except possibly at end) and without branch target or branch lables ( except possibly at the beginning )

## Slide 55: 2.7 Supporting Procedures in Computer Hardware
Procedure/function be used to structure programs
  A stored subroutine that performs a specific task based on the parameters with which it is provided
    easier to understand, allow code to be reused
  Six steps
  Place Parameters in a place where the procedure can access them
  Transfer control to the procedure：jump to
  Acquire the storage resources needed for the procedure (保护过程要用的寄存器)
  Perform the desired task
  Place the result value in a place where the calling program can access it
  Return control to the point of origin (即断点)

## Slide 56
Registers for procedure calling
  $a0 ~ $a3: four argument registers to pass parameters
  $v0 ~ $v1: two value registers to return values
  $ra: one return address register to return to origin point
Instruction for procedures: jal ( jump-and-link )
Caller jal ProcedureAddress
Callee jr $ra
Using more registers
  Stack: ideal data structure for spilling registers
    Push, pop
    Stack pointer ( $sp )
PC+4→$ra
Special registers

## Slide 57
57
MIPS STACKS Grow from higher address to lower address:
Push : sp=sp-4
Pop:sp=sp+4
SP=SP-4
SP=SP+4
STACK

## Slide 58
Example 2.15 Compiling a leaf procedure
( Assume: g ~ j -- $a0 ~ $a3 f -- $s0)
  C code:
  int leaf_example ( int g, int h, int i, int j )
  {
  int f ;
  f = ( g + h ) - ( i + j ) ;
  return f ;
  }
  MIPS assembly code:
  subi $sp, $sp,12 # adjust stack to make room for 3 items
  sw $t1, 8($sp) #These three instructions save three
  sw $t0, 4($sp) # register $t1,$t0,$s0
  sw $s0, 0($sp) # Let’s consider why it need to be done.
Save value
Return value
($t1)
($t0)
($s0)
$sp(-12)
High address
Low address
PUSH

## Slide 59: The values of the stack pointer and stack before, during and after procedure call in Example 2.15
$sp
a
.
b
.
c
.
Content of register $t1
Content of register $t0
Content of register $s0
$sp
$sp
High address
Low address

## Slide 60
add $t0, $a0, $a1 # register $t0 contains g + h
add $t1, $a2, $a3 # register $t1 contains i + j
sub $s0, $t0, $t1 # f = $t0 - $t1, which is ( g + h ) – ( i + j )
add $v0, $s0, $zero # returns f ( $v0 = $s0 + 0)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
lw $t1, 8($sp) # restore register $t1 for caller
add $sp, $sp, 12 # adjust stack to delete 3 items
jr $ra # jump back to calling routine
But maybe some of the three are not used by the caller
  So, this way might be inefficient
  Two classes of registers
    $t0 ~ $t9: 10 temporary registers , not preserved
    $s0 ~ $s7: 8 saved registers, must be preserved
POP

## Slide 61
Registers
The 32 MIPS registers are partitioned as follows:
  Register 0 : $zero always stores the constant 0
  Regs 2-3 : $v0, $v1 return values of a procedure
  Regs 4-7 : $a0-$a3 input arguments to a procedure
  Regs 8-15 : $t0-$t7 temporaries
  Regs 16-23: $s0-$s7 variables
  Regs 24-25: $t8-$t9 more temporaries
  Reg 28 : $gp global pointer
  Reg 29 : $sp stack pointer
  Reg 30 : $fp frame pointer
  Reg 31 : $ra return address

## Slide 62: Nested Procedures
Example 2.16 Compiling a recursive procedure ( Assume: n -- $a0 )
  C code for n!
  int fact ( int n )
  {
  if ( n < 1 ) return ( 1 ) ;
  else return ( n * fact ( n - 1 ) ) ;
  }
  Assume MAIN program: jal fact # n=2
  断点返回1000
  设主程序:
  996: Jal fact
  1000: add $s1, $s2, $s3

## Slide 63
63
  MIPS assembly code fact:
  Fact: addi $sp,$sp,-8 # adjust stack for 2 items
  sw $ra, 4($sp) # save the return address
  sw $a0, 0($sp) # save the argument n
slti $t0, $a0, 1 # test for n < 1
beq $t0, $zero, L1 # if n >= 1, go to L1
add $v0, $zero, 1 # return 1
add $sp, $sp, 8 # pop 2 items off stack
jr $ra # return to after j
L1: addi $a0, $a0, -1 # n >= 1, n=n-1
jal fact # call fact with ( n - 1 )
2000 : lw $a0, 0($sp) # return form jal: restore argument n
lw $ra, 4($sp) # restore the return address
addi $sp, $sp, 8 # adjust stack pointer to pop 2 items
mul $v0, $a0, $v0 # return n * fact ( n - 1 )
jr $ra # return to the caller

## Slide 64
64
Assume Main code is:
996: jal fact
1000: add $s1,$s2,$s3
And L1=1992(十进制)
Preserved things across a procedure call
Saved registers( $s0 ~ $s7 ), stack pointer register( $sp ),
return address register( $ra )
Not preserved things across a procedure call
Temporary registers( $t0 ~ $t9 )
主程序传递给子程序的
argument registers( $a0 ~ $a3 )
return value registers( $v0 ~ $v1)

## Slide 65
65
SP
SP-16
1000
2
1
2000
1000
2
1
2000
SP-16
1000
2
SP-8
初始 主程序第一次 第一次递归调用 第二次递归调用 N<1时
CALL FACT FACT FACT
SP-24
1000
2
1
2000
2000
0

## Slide 66: Disadvantages of recursion
Use too much resource，to protect the processor status，recursion may result in stack overflow.
Need push and pop，takes a lot of memory space leading to inefficient usage of memory.
How to avoid ? use loop instead of recursion.

## Slide 67: Stack allocation before, during and after procedure call

## Slide 68
Storage class of C variables
  automatic
  static
Procedure frame and frame pointer ( $fp )
  The importance of $fp
  automatic
Global pointer ( $gp )
  static

## Slide 69
Allocating Space for New Data on the Stack
  Procedure frame/activation record
    The segment of stack containing a procedure’s saved registers and local variables
  Frame pointer
    A value denoting the location of saved register and local variables for a given procedure
$fp→
$sp→
$fp→
$sp→
High address
Low address
$fp→
$sp→
Saved argument
Registers (if any)
Saved return address
Local arrays and
structures(if any)
a
b
c

## Slide 70
Allocating Space for New Data on the Heap

## Slide 71: MIPS operands
Name | Register no. | Usage | Preserved on call
$zero | 0 | The constant value 0 | n,.a.
$v0-$v1 | 2-3 | Values for results and expression evaluation | no
$a0-$a3 | 4-7 | Arguments | no
$t0-$t7 | 8-15 | Temporaries | no
$s0-$s7 | 16-23 | Saved | yes
$t8-$t9 | 24-25 | More temporaries | no
$gp | 28 | Global pointer | yes
$sp | 29 | Stack pointer | yes
$fp | 30 | Framer pointer | yes
$ra | 31 | Return address | yes
Name | Example | Comments
32 register | $s0,$s1……,$s7 $t0, $t1…….,$t7 | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. Registers $s0-$s7 map to 16-23 and $t0-$t7 map to 8-15.
230 memory words | Memory[0],Memory[4] , Memory[8] , …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr., so sequential word addr. Differ by 4. Memory holds data structures,arrays, and spilled registers.

## Slide 72: MIPS assembly language
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | Add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | Sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
logical | and | and $s1,$s2,$s3 | $s1=$s2 & $s3 | three reg. operands;bit-by-bit AND
 | or | or $s1,$s2,$s3 | $s1=$s2 ¦ $s3 | three reg. operands;bit-by-bit OR
 | nor | nor $s1,$s2,$s3 | $s1=~($s2 ¦ $s3) | three reg. operands;bit-by-bit NOR
 | and immediate | addi $s1,$s2,100 | $s1=$s2 & 100 | Bit-by-bit AND reg with constant
 | or immediate | ori $s1,$s2,100 | $s1=$s2 ¦ 100 | Bit-by-bit OR reg with constant
 | shift left logical | sll $s1,$s2,10 | $s1=$s2 << 10 | Shift left by constant
 | shift right logical | srl $s1,$s2,10 | $s1=$s2 >> 10 | Shift right by constant
Conditional branch | branch on equal | beq $s1,$s2,L | If($s1==$s2) go to L | Equal test and branch
 | branch not eaqal | bne $s1,$s2,L | If($s1!=$s2) go to L | Not equal test and branch
 | set on less than | slt $s1,$s2,$s3 | If($s2<$s3) $s1=1 Else $s1=0 | Compare less than;used with beq, bne
 | set on less than immediate | slt $s1,$s2100 | If($s2<100) $s1=1 Else $s1=0 | Compare less than immediate; used with beq, bne
Uncondition-al jump | jump | j L | go to L | Jump to target address
 | jump register | jr $ra | go to $ra | For procedure return
 | jump and link | jal L | $ra=PC+4; go to L | For procedure call

## Slide 73: MIPS machine language
Name | Format | Example |  |  |  |  |  | Comment
add | R | 0 | 18 | 19 | 17 | 0 | 32 | add $s1, $s2, $s3
sub | R | 0 | 18 | 19 | 17 | 0 | 34 | sub $s1, $s2, $s3
lw | I | 35 | 18 | 17 | 100 |  |  | lw $s1, 100($s2)
sw | I | 43 | 18 | 17 | 100 |  |  | sw $s1, 100($s2)
and | R | 0 | 18 | 19 | 17 | 0 | 36 | and $s1, $s2, $s3
or | R | 0 | 18 | 19 | 17 | 0 | 37 | or $s1, $s2, $s3
nor | R | 0 | 18 | 19 | 17 | 0 | 39 | nor $s1, $s2, $s3
addi | I | 12 | 18 | 17 | 100 |  |  | addi $s1, $s2,100
ori | I | 13 | 18 | 17 | 100 |  |  | ori $s1, $s2,100
sll | R | 0 | 0 | 18 | 17 | 10 | 0 | sll $s1, $s2,10
srl | R | 0 | 0 | 18 | 17 | 10 | 2 | srl $s1, $s2,10
beq | I | 4 | 17 | 18 | 25 |  |  | beq $s1, $s2,100
bne | I | 5 | 17 | 18 | 25 |  |  | bne $s1, $s2,100
slt | R | 0 | 18 | 19 | 17 | 0 | 42 | slt $s1, $s2,$s3
j | J | 2 | 2500 |  |  |  |  | j 10000(see section 2.9)
jr | R | 0 | 31 | 0 | 0 | 0 | 8 | j Sra
jal | J | 3 | 2500 |  |  |  |  | jar 10000(see section 2.9)
Field size |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | R | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | I | op | rs | rt | address |  |  | Data transfer ,branch format

## Slide 74
Summary of procedure
The jal instruction is used to jump to the procedure and
save the current PC (+4) into the return address register
Arguments are passed in $a0-$a3; return values in $v0-$v1
Since the callee may over-write the caller’s registers,
relevant values may have to be copied into memory
Each procedure may also require memory space for
local variables – a stack is used to organize the memory
needs for each procedure

## Slide 75: 最经典的黑客技术原理-缓冲区溢出
微机中，没有a0-a3，传递参数都是通过堆栈
函数调用将压入堆栈以下数据：ra，sfp，参数。
main() {
…
fun(a);
}
fun(int b){
char c[4];
printf(“%x\n”,c[4]);
c[12]=c[13]=c[14]=c[15]=0x40;
}
ra
Sfp
a
C[4]
微机的汇编：ret，函数返回