## Slide 1: Computer Organization & Design The Hardware/Software Interface
刘海风
Asso. Prof. Haifeng Liu
College of Computer Science and Technology, Zhejiang University
haifengliu@zju.edu.cn
计算机组成与设计
Chapter 2 – Part II
Instructions ：Language of the Machine

## Slide 2: 2.8 Communicating with People Beyond Numbers
ASCII ( American Standard Code for Information Interchange )
Instructions for moving bytes in MIPS
  Load byte ( lb ): lb $t0, 0($sp) # read byte from source
  Store byte ( sb ): sb $t0, 0($sp) # write byte to destination
Three choices for representing a string
  Place the length of the string in the first position
  An accompanying variable which indicate the length
  A character in the last position to mark the end of a string
C uses the third choice
  Terminate a string with a byte whose value is 0 ( null in ASCII )

## Slide 3
Example 2.17 Compiling a string copy procedure
( Assume: base addresses for x and y -- $a0 and $a1 i -- $s0 )
  C code：Y→X
  void strcpy ( char x[ ] , char y[ ] )
  { int i ;
  i = 0 ;
  while ( ( x[ i ] = y[ i ] ) !=“\ 0” ) /* copy and test byte */
  i += 1 ;
  }
  MIPS assembly code:
  strcpy: sub $sp, $sp, 4 # adjust stack for 1 more item
  sw $s0, 0($sp) # save $s0
  add $s0, $zero, $zero # i = 0 + 0
  L1: add $t1, $a1, $s0 # address of y[ i ] in $t1
  lb $t2, 0($t1) # $t2 = y [ i ]
  add $t3, $a0, $s0 # address of x[ i ] in $t3
  sb $t2, 0($t3) # x[ i ] = y[ i ]

## Slide 4
addi $s0, $s0, 1 # i = i + 1
bne $t2, $zero, L1 # if y[ i ] != 0, go to L1
lw $s0, 0($sp) # y[ i ] = = 0: end of string;
# restore old $s0
add $sp, $sp, 4 # pop 1 word off stack
jr $ra # return
Optimization for example 2.17
  strcpy is a leaf procedure
  Allocate i to a temporary register $t0
For a leaf procedure
  The compiler exhausts all temporary registers
  Then use the registers it must save

## Slide 5: 2.9 MIPS Addressing for 32-Bit Immediate and Addresses
32-Bit Immediate addressing
  most constants is short and fit into 16-bit field
  Set upper 16 bits of a constants in a register with load upper immediate (lui)
  lui $t0 , 255
Instruction |  |  | 
001111 | 00000 | 01000 | 0000 0000 1111 1111
Register |  |  | Filling with “0”
0000 0000 1111 1111 |  |  | 0000 0000 0000 0000

## Slide 6
Example 2.19 Loading a 32-bit constant
  The 32-bit constant:
  0000 0000 0011 1101 0000 1001 0000 0000 (61*164 + 2304=4000000)10
  MIPS code:
  lui $s0, 61 # 61 decimal = 0000 0000 0011 1101 binary
  (The value of $s0 afterward is: 0000 0000 0011 1101 0000 0000 0000 0000)
  addi $s0, $s0, 2304 # 2304 decimal = 0000 1001 0000 0000 binary
  (The value of $s0 afterward is: 0000 0000 0011 1101 0000 1001 0000 0000)
Note：Why does it need two steps?
The reserved register $at for the assembler

## Slide 7
Addressing in branches and jumps
  For jumps: J-format
    Example:
  j 10000 # go to location 10000
  | 2 | 10000 |
  6 bits 26 bits
    Pseudo-direct addressing
    26 bits of the instruction concatenated with the upper 4 bits of PC
  For branches:
    Example:
    bne $s0, $s1, Exit # go to Exit if $s0 != $s1
  | 5 | 16 | 17 | Exit |
  6 bits 5 bits 5 bits 16 bits
    PC-relative addressing
    PC = (PC + 4) + Branch address

## Slide 8
Example 2.20 Show branch offset in machine language
  C language: while (save[i]==k) i=i+j; MIPS assembler code in Example 2.12:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s6 # $t1 = address of save[i]
  lw $t0, 0($t1) # temp reg $t0 = save[i]
  bne $t0, $s5, Exit # go to Exit if save[i] != k
  add $s3, $s3, $s4 # i = i + j
  j Loop # go to Loop
  Exit:

## Slide 9
  Assembled instructions and their addresses:
80000 | 0 | 19 | 19 | 9 | 0 | 32 |
80004 | 0 | 9 | 9 | 9 | 0 | 32 |
80008 | 0 | 9 | 22 | 9 | 0 | 32 |
80012 | 35 | 9 | 8 | 0 |
80016 | 5 | 8 | 21 | 2 (8) |
80020 | 0 | 19 | 20 | 19 | 0 | 32 |
80024 | 2 | 20000 (80000) |
80028 . . .
80028 – 80020 =8
  Modification:
    All MIPS instructions are 4 bytes long
    PC-relative addressing refers to the number of words
    The address field at 80016 above should be 2 instead of 8
add
add
add
Lw
bne
add
j
PC+4+offset=80028
Loop:
Exit:

## Slide 10
While branch target is far away
  Inserts an unconditional jump to target
  Invert the condition so that the branch decides whether to skip the jump
Example 2.21 Branching far away
  Given a branch:
  beq $s0, $s1, L1
  Rewrite it to offer a much greater branching distance:
    bne $s0, $s1, L2
    j L1
    L2:

## Slide 11
MIPS addressing summary
  Register addressing:
    add $s0,$s0,$s0
  Base or displacement addressing:
    lw $s1,0($s0)
  Immediate addressing:
    addi $s0,$s0,4
  PC-relative addressing:
    beq $s0,$s1,L1
  Pseudodirect addressing:
    j Address1

## Slide 12: Five MIPS addressing modes

## Slide 13
Example 2.22 Decoding machine code
  Machine instruction
  ( Bits: 31 28 26 5 2 0 )
  0000 0000 1010 1111 1000 0000 0010 0000
  Decoding
    Determine the operation from opcode
    op: 000000  R-format instruction
    op rs rt rd shamt funct
  | 000000 | 00101 | 01111 | 10000 | 00000 | 100000 |
    funct: 100000  add instruction
    Determine other fields
    rs: $a1; rt: $t7; rd: $s0 p135-P136
    Show the assembly instruction
    add $s0, $a1, $t7 (Note: add rd,rs,rt)

## Slide 14: Summary of MIPS architecture in Chapter 2
MIPS instruction format
MIPS operands
MIPS assembly language
  Arithmetic
    add add $s1, $s2, $s3
    subtract sub $s1, $s2, $s3
    add immediate addi $s1, $s2, -3 (Note:subi does not exist)
Name | Fields |  |  |  |  |  | Comments
Field size | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | op | rs | rt | address/immediate |  |  | Transfer,branch,imm. format
J-format | op | target address (word) |  |  |  |  | Jump instruction format
Name | Example
32 registers | $s0~$s7, $t0~$t9,$zero, $a0~$a3, $v0~$v1, $gp $fp, $gp, $ra, $at
Mem words | ¦ Memory[0], Memory[4], Memory[4], . . . , Memory[4294967292]

## Slide 15
  Data transfer
    load word lw $s1, 100($s2)
    store word sw $s1, 100($s2)
    load byte lb $s1, 100($s2)
    store byte sb $s1, 100($s2)
    load upper immediate lui $s1, 100
  Conditional branch
    branch on equal beq $s1, $s2, 25
    branch on not equal bne $s1, $s2, 25
    set on less than slt $s1, $s2, $s3
    set on less than immediate slti $s1, $s2, 100
  Unconditional jump
    jump j 2500
    jump register jr $ra
    jump and link jal 2500
(Why not beqi?)

## Slide 16: Tips on Assembler
Principle：
  It’s not requisite to obey the conventions
Example
  Jump back from procedure instead of using Jr ra
  Jump into or out of a procedure directly.
What could you do if there are more than 4 parameters for the procedure?
Push the parameters into the stack before Jal and then pop it out in the procedure.
Use free register to transfer the parameter

## Slide 17: 2.10 Translanting and starting a Program
A translation hierarchy

## Slide 18: Start a C program in a file on disk to run
Compiling
  C program  assembly language program
Assembling
  Assembly language program  machine language module
  pseudoinstructions
    move $t0,$t1 # register St0 gets register $t1
    add $t0,$zero, $t1 # register St0 gets 0+register $t1
  Symbol table
    A table that matches name of labels to the addresses of the memory words that instructions occupy.
object file

## Slide 19
  Object file of UNIX (six distinct pieces)
    object file header—size and position of the other pieces
    Text segment
    static data segment and dynamic data
    The relocation information -- Identifies absolute addresses of instruction and data words when the program is loaded into memory
    Symbol table
    debugging information
Object file header |  |  | 
 | Name | Procedure A | 
 | Text size | 100hex | 
 | Data size | 20hex | 
Text segment | Address | instruction | 
 | 0 | lw $a0, 0($gp) | 
 | 4 | jal 0 | 
 | …… | -- | 
Data segment | 0 | (X) | 
 | …… | …… | 
Relocation information | Address | Instruction type | Dependency
 | 0 | Lw | X
 | 4 | jal | B
Symbol table | label | Address | 
 | X | -- | 
 | B | -- | 

## Slide 20
Linking
  Object modules(including library routine)  executable program
  3 step of Link
    Place code and data modules symbolically in memory
    Determine the addresses of data and instruction labels
    Patch both the internal and external references (Address of invoke)
Link object file A & B
MIPS memory allocation for program and data
0000000000000000 0111111111111111 + 215-1
0001000000000000 1000000000000000
1111111111111111 1000000000000000 -215
+
0001000000000000 0000000000000000
0
$sp
7fff fffchex
$gp
1000 8000hex
PC
0040 0000hex
Dynamic data
Stack
Static data
Reserved
Text
1000 0000hex

## Slide 21
21
Example 2.23 Linking object files

## Slide 22
22
Address of X:
1000 8000 + FFFF 8000 = 1000 0000
Address of Y:
1000 8000 + FFFF 8020 = 1000 0020
微机的执行文件：
Com
Exe
PE

## Slide 23
Loading
  Determine size of text and data segments
  Create an address space large enough
  Copy instructions and data from executable file to memory
  Copy parameters (if any) to the main program onto the stack
  Initialize registers and set $sp to the first free location
  Jump to a start-up routine

## Slide 24: 执行文件与进程
24
执行文件
  在硬盘上，非执行态
  如病毒样本
进程
  转载到内存
  可以细分为多个可以并发执行的线程
  如激活态病毒
  如何看进程: 任务管理器

## Slide 25: 计算机任何动作都是程序设计的
25
病毒
  组成：感染能力（自我复制），隐藏，破坏能力
  一个简单的
    感染：看到一个执行程序，就把病毒程序拷贝到执行程序最后，程序启动时加一条无条件跳转指令，跳到病毒处，病毒程序执行完成跳回首地址后
    隐藏：把执行程序拆封为n个，运行时组装为一体
    破坏：随便
程序都需要消耗内存
  System idle 也是程序，也消耗内存

## Slide 26: EXE文件转移
26
把EXE的代码段中的一个字节写成00
在运行时，用计算结果(或其他来源)写入该位置
作用：防拷贝
参考：经典的针孔加密方法
  用针在磁盘上打孔，则该扇区的属性为坏块，以此为正版标记
  如果是磁盘拷贝的，则该块为CRC校验错误

## Slide 27: EXE文件加密
27
输入密码才能执行该文件？
普通的方法，先读密码，验证后判断是否继续
  问题：简单的修改执行文件即可破解
一般方法：
  第一段代码是密码验证
  若通过，则解密后续代码
    解密后长度=加密前，简单
    随便压缩
高级方法：
  分段加密，前一段的中间结果作为后续的解密用的密钥

## Slide 28: 2.13 A C Sort Example to Put it All Together
Three general steps for translating C procedures
  Allocate registers to program variables
  Produce code for the body of the procedures
  Preserve registers across the procedures invocation
Procedure swap
  C code
  swap ( int v[ ] , int k )
  {
  int temp ;
  temp = v[ k ] ;
  v[ k ] = v[ k + 1 ] ;
  v[ k + 1 ] = temp ;
  }

## Slide 29
  Register allocation for swap
  v ---- $a0 k ---- $a1 temp ---- $t0
  swap is a leaf procedure, nothing to preserve
  MIPS code for the procedure swap
    Procedure body
  swap: sll $t1, $a1, 2 # $t1 = k * 4
  add $t1, $a0, $t1 # $t1 = v + ( k * 4 )
  # $t1 has the address of v[ k ]
  lw $t0, 0($t1) # $t0 ← v[ k ]
  lw $t2, 4($t1) # $t2 ← v[ k + 1 ]
  sw $t2, 0($t1) # v[k+1]) → v[ k ]
  sw $t0, 4($t1) # v[k] → v[ k + 1 ]
    Procedure return
  jr $ra # return to calling routine

## Slide 30
Procedure sort
  C code
  sort ( int v[ ] , int n )
  { int i , j ;
  for ( i = 0 ; i < n ; i + = 1 ) {
  for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j- = 1 )
  swap ( v , j ) ;
  }
  }
  Register allocation for sort
  v -- $a0 n -- $a1 i -- $s0 j -- $s1
  Passing parameters in sort
  Preserving registers in sort
  $ra , $s0, $s1, $s2, $s3
V[0]
V[1]
V[2]
……
V[n-1]
If V[0]> V[1]
i
j

## Slide 31
  Code for the procedure sort
    Saving registers
  sort: addi $sp, $sp, -20 # make room on stack for 5 registers
  sw $ra, 16($sp) # save $ra on stack
  sw $s3, 12($sp) # save $s3 on stack
  sw $s2, 8($sp) # save $s2 on stack
  sw $s1, 4($sp) # save $s1 on stack
  sw $s0, 0($sp) # save $s0 on stack
    Procedure body{Outer loop {Inner loop} }
    Restoring registers
    exit1: lw $s0, 0($sp) # restore $s0 from stack
    lw $s1, 4($sp) # restore $s1 from stack
    lw $s2, 8($sp) # restore $s2 from stack
    lw $s3, 12($sp) # restore $s3 from stack
    lw $ra, 16($sp) # restore $ra from stack
    addi $sp, $sp, 20 # restore stack pointer
    Procedure return
    jr $ra # return to calling routine

## Slide 32
    Code for Procedure body
      Outer loop—first for loop
    for ( i = 0 ; i < n ; i + = 1 ) {
      Move parameters
      move $s2, $a0 # $s2 ← $a0 ($a0: base address)
      move $s3, $a1 # $s3 ← $a1 ($a1: array size)
      Outer loop
      move $s0, $zero # $s0 ← $zero ( i = 0)
  for1tst: slt $t0, $s0, $s3 # test if $s0 >= $s3 (i >= n)
      beq $t0, $zero, exit1 # go to exit1 if $s0 >= $s3 (i >= n)
      ………………
      （body of first for loop is second for loop）
      ………………
  exit2: addi $s0, $s0, 1 # i = i + 1
  j for1tst # jump to test of outer loop
  exit1:

## Slide 33
      Inner loop-- second for loop is body of first for loop
    for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j- = 1 ){
      addi $s1, $s0, -1 # j = i - 1
for2tst: slti $t0, $s1, 0 # test if j < 0
    bne $t0, $zero, exit2 # go to exit2 if j < 0
    sll $t1, $s1, 2 # $t1 = j * 4
    add $t2, $s2, $t1 # $t2 = the address of v[j]
    lw $t3, 0($t2) # $t3 = v[j]
    lw $t4, 4($t2) # $t4 = v[j + 1]
    slt $t0, $t4, $t3 # test if v[j+1]>=v[j]
    beq $t0, $zero, exit2 # go to exit2 if v[j+1]>=v[j]
      ………………
      （body of first for loop ）
    ………………
    addi $s1, $s1, -1 # j = j - 1
    j for2tst # jump to test of inner loop
  exit2:

## Slide 34
      body of first for loop
      Pass parameters and call
    move $a0，$s2 # $a0←$s2 ($s2 : base address of the array )
    move $a1，$s1 # $a1←$s1 ($a1← j)
      Call function swap(int v[],int k)
    jal swap # ($a0 might be changed in swap)
Notice: 1.Why are $a0 and $a1 saved? $a0 is the base of the array v. $a0 will be used repeatedly and might be(actually not here) changed by the procedure swap. $a1 is the size of the array v. $a1 will be used repeatedly and changed before the procedure swap is called. 2.Why are they not pushed to stack?
  Register variable is faster
The Full Procedure

## Slide 36: s0, t0
36
父函数保证：子函数能随便使用t0-t9，返回给父函数的时候，t0-t9可以随便改变
子函数保证：返回给父函数的时候，s0-s7保持父函数调用子函数的值

## Slide 37: 2.15 Arrays versus Pointers
Two C procedures
  Array version
clear1 ( int array[ ], int size )
  { int i;
  for ( i = 0 ; i < size ; i = i + 1 )
  array[i] = 0;
  }
  Pointer version
    clear2 ( int *array, int size )
    {
    int *p;
    for ( p = &array[0] ; p < &array[size] ; p = p + 1 )
    *p = 0;
    }

## Slide 38
Assembly code for clear-1 procedure (array version)
  move $t0, $zero # i = 0
  loop1: sll $t1, $t0, 2 # $t1 = i * 4
  add $t2, $a0, $t1 # $t2 = address of array[ i ]
  sw $zero, 0($t2) # array[ i ] = 0
  addi $t0, $t0, 1 # i = i +1
  slt $t3, $t0, $a1 # test if i < size
  bne $t3, $zero, loop1 # if ( i < size ) go to loop1
  jr $ra
  This code works as long as size is greater than 0. (In this case,the loop will be executed once even though the value of the size parameter is invalid. Actually,size >0 must be checked at first)

## Slide 39
Assembly code for clear-2 procedure (pointer version)
  move $t0, $a0 # p = the start address of the array[]
  sll $t1, $t1, 2 # $t1 = size * 4
  add $t2, $a0, $t1 # $t2 = &array[size](address of array[size] )
  loop2: sw $zero, 0($t0) # Memory[ p ] = 0
  addi $t0, $t0, 4 # p = p + 4
  slt $t3, $t0, $t2 # $t3 = (p < &array[size] )
  bne $t3, $zero, loop2 # if ( p < &array[size] ) go to loop2
  jr $ra
  This code works as long as size is greater than 0.
Compare the two versions
  Array version has the “multiply” and add inside loop
  Pointer version reduces instructions/iteration from 6 to 4
For modern compliers, both ways are the same

## Slide 40: 2.16 Real Stuff: IA-32 Instructions
The IBM/Motorola PowerPC
  Similarities with MIPS:
    All instructions are 32 bits long
    32 integer registers
    Data transfer is possible only with loads and stores
  Indexed addressing
    MIPS code
    add $t0, $a0, $s3 # $a0 has base of an array, $s3 is index
    lw $t1, 0($t0) # $t1 gets Memory[$a0 + $s3]
    Equivalent code in PowerPC
    lw $t1, $a0 + $s3 # $t1 gets Memory[$a0 + $s3]
  Update addressing
    MIPS code
    lw $t0, 4($s3) # $t0 = Memory[$s3 + 4]
    addi $s3, $s3, 4 # $s3 = $s3 + 4
    Equivalent code in PowerPC
    lwu $t0, 4($s3) # $t0 = Memory[$s3 + 4] ; $s3 = $s3 + 4

## Slide 41: Indexed and update addressing mode
41

## Slide 42
42
  Unique PowerPC instructions
    Load multiple and store multiple
    Instruction bc for loop
      C code
      for ( i = n ; i != 0 ; i = i - 1 ) { . . . }
      MIPS instructions
      Loop: . . .
      addi $t0, $t0, -1 # $t0 = $t0 - 1
      bne $t0, $zero, Loop # if $t0 != 0 go to Loop
      PowerPC instructions
      bc Loop, ctr != 0 # $ctr = $ctr - 1 ; if $ctr != 0 go to Loop
      Problems with the complex instructions above
    The instructions may not exactly match what the compiler needs
    A common case may be slower than a simple sequence

## Slide 43: The Intel 80x86
The milstones
  1978 intel 8086
    16-bit architecture
    Is not considered a general-purpose register
  1980 intel 8087 floating-point coprocessor
  1982 80286 extended the 8086 architecture by
    Increasing Address Space to 24 bits
    Manipulate the protection model
  1985 80386 extended the 80286 architecture
    32-bit architecture with 32-bit registers
    32-bit address space
    Add paging support in addition to segmented addressing
    Nearly a general-purpose register machine ?

## Slide 44
  1989~95 Higher performance
    80486 in 1989
    Pentium in 1992
    Pentium Pro in 1995
  1997 Expand Pentium and Pentium Pro with MMX
  1999 Expand Pentium with SSE(SIMD) as Pentium III
    8 separate registers ,double their width to 128 bits
    Add a single-precision floating-point data type
    4 32-bit floating-point operations can be performed in parallel
    Cache prefetch instructions
  2001 Intel Pentium 4
  2003 A company other than Intel enhanced the IA-32 architecture
    AMD
    Executing all IA-32 instructions with 64-bit Address space & data
  2004 Intel capitulates and embraces AMD64

## Slide 45
80x86 registers and data addressing modes
    80386 extended all 16-bit registers but segment ones to 32 bits
    GPR ( general-purpose register )
    Addressing modes
      Register indirect
      Based mode with 8- or 32-bit displacement
      Base plus scaled index
      Base plus scaled index with 8- or 32-bit displacement
80x86 integer operations
    Data movement instructions
    Arithmetic and logic instructions
    Control flow
    String instructions

## Slide 46: IA-32 Register and Data Addressing Modes
Name | Register no. | Usage
$zero | 0 | The constant value 0
$v0-$v1 | 2-3 | Values for results and expression evaluation
$a0-$a3 | 4-7 | Arguments
$t0-$t7 | 8-15 | Temporaries
$s0-$s7 | 16-23 | Saved
$t8-$t9 | 24-25 | More temporaries
$gp | 28 | Global pointer
$sp | 29 | Stack pointer
$fp | 30 | Framer pointer
$ra | 31 | Return address

## Slide 47: Instruction types for ALU & data transfer
Source/destination operand type | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate

## Slide 48: Some typical IA-32 Integer Operations

## Slide 49: Typical 80x86 instruction format
1Byte
5Bytes
3Bytes
1Bytes
5Bytes
6Bytes

## Slide 50: 2.18 Concluding Remarks
Two principles of stored-program computers
  Use instructions as numbers
  Use alterable memory for programs
Four design principles
  Simplicity favors regularity
  Smaller is faster
  Make the common case fast
  Good design demands good compromises
MIPS instruction set

## Slide 51: 2.19 History of Instruction Set Development
Accumulator Architectures
  Only 1 register for arithmetic instructions: accumulator
  Memory-based operand-addressing mode
Example 2.23 Compiling C code to accumulator instructions
  C code: A = B + C ;
  Accumulator instructions:
    load AddressB # Acc = Memory[AddressB], or Acc = B
    add AddressC # Acc = Acc + Memory[AddressC], or Acc = B + C
    store AddressA # Memory[AddressA] = Acc, or A = B + C
Extended Accumulator Architectures

## Slide 52
General-Purpose Register Architectures
  Register-memory architecture
    80386
    IBM 360
  Load-store or register-register architecture
    CDC 6600
    MIPS
  DEC’s VAX architecture
    Allow any combination of registers and memory operands
    Memory-memory architecture
Example 2.24 Compiling C code to memory-memory instructions
  C code: A = B + C;
  instructions:
    add AddressA, AddressB, AddressC

## Slide 53
Compact Code and Stack Architectures
  Variable-length instructions
    To match the varying operand specifications
    To minimize code size
  Stack model of execution
    All registers are abandon, so the instructions are short.
    Push, pop
Example 2.25 Compiling C code to stack instructions
  C code: A = B + C;
  Stack instructions:
    push AddressC # Top = Top+4; Stack[Top]=Memory[AddressC]
    push AddressB # Top = Top+4; Stack[Top]=Memory[AddressB]
    add # Stack[Top-4]= Stack[Top]+Stack[Top-4];Top=Top-4;
    pop AddressA # Memoryp[AddressA]=Stack[Top]; Top=Top-4;

## Slide 54
High-Level-Language Computer Architecture
  Goal: hardware more like programming languages
  Finally failed
Reduced Instruction Set Computer Architecture (RISC )
  Fixed instruction lengths
  Load-store instruction sets
  Limited addressing modes
  Limited operations
  MIPS, Sun SPARC, Hewlett-Packard PA-RISC
  IBM PowerPC, DEC Alpha

## Slide 55
END