## Slide 1: Computer Organization & Design The Hardware/Software Interface
Haifeng Liu
College of Computer Science and Technology, Zhejiang University
haifengliu@zju.edu.cn
计算机组成与设计
Chapter 5
The processor : Datapath and control

## Slide 2: Computer Organization
Computer
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……

## Slide 3: Contents of Chapter 5
5.1 Introduction & Logic Design Conventions
5.2 Building a datapath
5.3 A Simple Implementation Scheme
5.4 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 4: Teaching prototype: MIPS
Microprocessor
without
Interlocked
Pipeline
Stages
What is the MIPS?

## Slide 5: 5.1 Introduction
We‘ll look at an implementation of the MIPS
Simplified to contain only:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
An Overview of the implementation
  For every instruction, the first two step are identical
    Fetch the instruction from the memory
    Decode and read the registers
  Next steps depend on the instruction class
    Memory-reference Arithmetic-logical branches
What are steps?
How many FUN.?

## Slide 6: Simple Implementation
Include the functional units we need for each instruction
Why do we need this stuff?
A
L
U
c
o
n
t
r
o
l
R
e
g
W
r
i
t
e
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
W
r
i
t
e
d
a
t
a
A
L
U
r
e
s
u
l
t
A
L
U
D
a
t
a
D
a
t
a
R
e
g
i
s
t
e
r
n
u
m
b
e
r
s
a
.
R
e
g
i
s
t
e
r
s
b
.
A
L
U
Z
e
r
o
5
5
5
3

## Slide 7: Basic elements
Basic logic gate。
  AND：S=A•B
  OR ：S=A+B
  NOT：S=~A
A | B | A•B | A+B | ~A
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 8: MUX
多路开关：有若干个输入，由控制端决定那一路输入将输出。
  经常是多路并行。
C | S
0 | A
1 | B

## Slide 9: Adder
Half adder：
Full adder：S=A+B
  Input: A, B, C0. Output: Sum, CarryOut
  S = A ⊕ B ⊕ C
  C+1= A•B + B•C + C•A
A | 0 | 0 | 1 | 1
B | 0 | 1 | 0 | 1
S | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
B | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
C | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
S | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
C+1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1

## Slide 10: 串行进位加法器
4位串行进位加法器：S=A+B
  各位串行进行。
  同时根据结果产生各种标记状态。
+
Operation
A
S=A+B
32
B
32

## Slide 11: Adder
32-bit Adder
+
Operation
A
S=A+B
32
B
32

## Slide 12: ALU
算术逻辑运算器ALU：即运算器
  5 Operations
  “Set on less than”：
  if A<B then Result=1；
  else Result=0。
Operation | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Slt
Less
Binvert
Operation
CarryIn
CarryOut
Result
A
B
00
01
10
11
0
1
3
ALU
Operation
A
Result
32
B
32

## Slide 13: ALU Control
ALUop与Func联合对ALU的控制

## Slide 14: ALU Control
ALU控制：
  ALU由ALUcontrol控制：ALUcontrol由ALUop和指令的低6位(5-0)联合产生ALU控制码。
  这样的好处在于分级控制，对于用的最多的加、减操作，系统只需给出两位的ALUop即可。
Result
Operation
ALUop
ALU
control
Func
[5-0]
32
A
ALU
32
3
2
32
B
zero

## Slide 15: REGISTER
Register
  State element。
  Can be controled by Write signal.
Register
In
Out
Register
In
Out
Write
Read：
Out=Register
Write：
Register=In
Clock cycle

## Slide 16: Memory
存储器：
  可分为指令存储器与数据存储器；
  指令存储器设为只读；输入指令地址，输出指令。
  数据存储器可以读写，由MemRead和MemWrite控制。按地址读出数据输出，或将写数据写入地址所指存储器单元。
Instruction
Instruction
Address
Instruction
memory
MemWrite
Read
data
Address
Data
memory
Write
data
MemRead

## Slide 17: D 触发器
C
D
Q
Q
D
Q
C
Q
Symbol of Latch
C | D | Q(t + 1)
0 | X | hold
1 | 0 | Q=0：reset
1 | 1 | Q=1：set
C | D | S | R | Q(t + 1)
0 | X | X | X | hold
1 | 0 | 0 | 1 | Q=0：reset
1 | 1 | 1 | 0 | Q=1：reset
S
R
Truth table

## Slide 18: Register File
Register File：
  32 32-bit Registers；
  Input: 2 32-bit;
  Output: 32-bit data, 32-bit register number;
  Register write control。

## Slide 19: Register File
Write Register:
  we still use the real clock to determine when to write
Register
C
C
D
D
C
C
D
D
0
1
n-1
n
Register 1
Register n-1
Register n
Register number
Register data
Write
decoder

## Slide 20: Register File

## Slide 21: 32×32bits寄存器组硬件描述
Module regs(clk, rst,reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr, wdata, we, rdata_A, rdata_B);
input clk, rst, we;
input [4:0] reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr;
input [31:0] wdata;
output [31:0] rdata_A, rdata_B;
reg [31:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (reg_Rd_addr_A == 0)? 0 : register[reg_Rd_addr_A]; // read
assign rdata_B = (reg_Rt_addr_B == 0)? 0 : register[reg_Rt_addr_B]; // read
always @(posedge clk or posedge rst)
begin
if (rst==1) begin // reset
for (i=1; i<32; i=i+1)
register[i] <= 0;
end
else begin
if ((reg_Wt_addr != 0) && (we == 1)) // write
register[reg_Wt_addr] <= wdata;
end
end
endmodule

## Slide 22: 32个Register的功用
寄存器组有32个32位寄存器，其功用分配如下表：

## Slide 23: The other elements
Sign Extend：
  将16位的补码表示的有符号立即数，扩展为32位。
  方法：只需重复符号位即可。
Shift：
  Shift 2 bits left。
  方法：将输入高移2位接输出，输出的低两位接0。
16
32
Sign
extend
D15
D14
.
.
.
D00
D31
.
.
.
D16
D15
D14
.
.
.
D00
Shift
left 2
D31
D30
D29
.
.
.
.
.
.
D02
D01
D00
D31
D30
D29
.
.
.
.
.
.
D02
D01
D00

## Slide 24: An abstract view of the implementation of MIPS

## Slide 25: An abstract view of Simple implementation of MIPS

## Slide 26: Simple Implementation
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 27: Contents of Chapter 5
5.1 Introduction & Logic Design Conventions
5.2 Building a datapath
5.3 A Simple Implementation Scheme
5.4 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 28
Building a Datapath ……
Building The Elements
ALU & Registers

## Slide 29: MIPS fields (format)
op：basic operation of the instruction, traditionally called the opcode.
rs： the first register source operand.
rt： the second register source operand.
rd： the register destination operand.
shamt： shift amount.
funct： function,this field selects the specific variant of the operation in the op field.
Must bear in mind !
Field size | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | op | rs | rt | Imm/Word address |  |  | Data transfer ,branch format
J-format | op | target address (word) |  |  |  |  | Uncondition-al jump
Region: ±215

## Slide 30: The datapath there are ……
Name | Register no. | Usage | Preserved on call
$zero | 0 | The constant value 0 | n,.a.
$v0-$v1 | 2-3 | Values for results and expression evaluation | no
$a0-$a3 | 4-7 | Arguments | no
$t0-$t7 | 8-15 | Temporaries | no
$s0-$s7 | 16-23 | Saved | yes
$t8-$t9 | 24-25 | More temporaries | no
$gp | 28 | Global pointer | yes
$sp | 29 | Stack pointer | yes
$fp | 30 | Framer pointer | yes
$ra | 31 | Return address | yes
Name | Example | Comments
32 register | $s0-$s7,$t0-$t9, $zero, $a0-$a3,$v0-$v1,$sp,$ra | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. Registers $s0-$s7 map to 16-23 and $t0-$t7 map to 8-15.
230 memory words | Memory[0] Memory[4] …Memory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr., so sequential word addr. Differ by 4. Memory holds data structures,arrays, and spilled registers.

## Slide 31: MIPS assembly language
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | Add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | Sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
logical | and | and $s1,$s2,$s3 | $s1=$s2 & $s3 | three reg. operands;bit-by-bit AND
 | or | or $s1,$s2,$s3 | $s1=$s2 ¦ $s3 | three reg. operands;bit-by-bit OR
 | nor | nor $s1,$s2,$s3 | $s1=~($s2 ¦ $s3) | three reg. operands;bit-by-bit NOR
 | and immediate | addi $s1,$s2,100 | $s1=$s2 & 100 | Bit-by-bit AND reg with constant
 | or immediate | ori $s1,$s2,100 | $s1=$s2 ¦ 100 | Bit-by-bit OR reg with constant
 | shift left logical | sll $s1,$s2,10 | $s1=$s2 << 10 | Shift left by constant
 | shift right logical | srl $s1,$s2,10 | $s1=$s2 >> 10 | Shift right by constant
Conditional branch | branch on equal | beq $s1,$s2,L | If($s1==$s2) go to L | Equal test and branch
 | branch not eaqal | bne $s1,$s2,L | If($s1!=$s2) go to L | Not equal test and branch
 | set on less than | slt $s1,$s2,$s3 | If($s2<$s3) $s1=1 Else $s1=0 | Compare less than;used with beq, bne
 | set on less than immediate | slt $s1,$s2100 | If($s2<100) $s1=1 Else $s1=0 | Compare less than immediate; used with beq, bne
Uncondition-al jump | jump | j L | go to L | Jump to target address
 | jump register | jr $ra | go to $ra | For procedure return
 | jump and link | jal L | $ra=PC+4; go to L | For procedure call

## Slide 32: ALU OP for MIPS machine language
Name | Format | Example |  |  |  |  |  | Comment
add | R | 0 | 18 | 19 | 17 | 0 | 32 | add $s1, $s2, $s3
sub | R | 0 | 18 | 19 | 17 | 0 | 34 | sub $s1, $s2, $s3
lw | I | 35 | 18 | 17 | 100 |  |  | lw $s1, 100($s2)
sw | I | 43 | 18 | 17 | 100 |  |  | sw $s1, 100($s2)
and | R | 0 | 18 | 19 | 17 | 0 | 36 | and $s1, $s2, $s3
or | R | 0 | 18 | 19 | 17 | 0 | 37 | or $s1, $s2, $s3
nor | R | 0 | 18 | 19 | 17 | 0 | 39 | nor $s1, $s2, $s3
addi | I | 12 | 18 | 17 | 100 |  |  | addi $s1, $s2,100
ori | I | 13 | 18 | 17 | 100 |  |  | ori $s1, $s2,100
beq | I | 4 | 17 | 18 | 25 |  |  | beq $s1, $s2,100
bne | I | 5 | 17 | 18 | 25 |  |  | bne $s1, $s2,100
slt | R | 0 | 18 | 19 | 17 | 0 | 42 | slt $s1, $s2,$s3
j | J | 2 | 2500 |  |  |  |  | j 10000(see section 2.9)
jr | R | 0 | 31 | 0 | 0 | 0 | 8 | j Sra
jal | J | 3 | 2500 |  |  |  |  | jar 10000(see section 2.9)
Field size |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | R | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | I | op | rs | rt | address |  |  | Data transfer ,branch format

## Slide 33: Register File--Built using D flip-flops
Register files
  Foundation element of Computer（Part of Datapath ）
  Aggregation of many Registers
  Register address、Control signals: Read/Write

## Slide 34: Register File: Read-Output
  Output from the register
5 bits
5 bits
5 bits
32 bits
32 bits
32 bits
Reg. address
Reg. address
Data output

## Slide 35: Register File: Write-Input
  Written to the register
32 bits
rd or rt
5 bits
Reg. address
Write signals

## Slide 36
Description: 32×32bits Register files
Module regs(clk, rst,reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr, wdata, we, rdata_A, rdata_B);
input clk, rst, we;
input [4:0] reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr;
input [31:0] wdata;
output [31:0] rdata_A, rdata_B;
reg [31:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (reg_Rd_addr_A == 0)? 0 : register[reg_Rd_addr_A]; // read
assign rdata_B = (reg_Rt_addr_B == 0)? 0 : register[reg_Rt_addr_B]; // read
always @(posedge clk or posedge rst)
begin
if (rst==1) begin // reset
for (i=1; i<32; i=i+1)
register[i] <= 0;
end
else begin
if ((reg_Wt_addr != 0) && (we == 1)) // write
register[reg_Wt_addr] <= wdata;
end
end
endmodule

## Slide 37: Reg-files Simulation

## Slide 38
Building a Datapath ……
Data Stream of Datapath

## Slide 39: Instruction execution in MIPS
Fetch :
  Take instructions from the instruction memory
  Modify PC to point the next instruction
Instruction decoding & Read Operand:
  Will be translated into machine control command
  Reading Register Operands, whether or not to use
Executive Control:
  Control the implementation of the corresponding ALU operation
Memory access:
  Write or Read data from memory
  Only LW/SW
Write results to register:
  If it is R-type instructions, ALU results are written to Rd
  If it is I-type instructions, Results are written to Rt

## Slide 40: Instruction fetching three elements
PC
Add
Instruction memory
Program counter
Adder
How to connect? Who?
Data Stream of Instruction fetching
Read address
Instruction
Instruction
Memory

## Slide 41: Instruction fetching unit
PC
4
CPU
Read address
Instruction
Instruction
Memory
add
Instruction
Instruction Register
  Can you omit it?

## Slide 42: How simple is!
Why PC+4?

## Slide 43: More Implementation Details
Abstract / Simplified View:

## Slide 44: Path Built using Multiplexer
R-type instruction Datapath
I-type instruction Datapath
  For ALU
  For memory
  For branch
J-type instruction Datapath
  For Jump
First, Look at the data flow within instruction execution
Data Stream of Instruction executing

## Slide 45: R type Instruction & Data stream
op(6)
rs(5)
rt(5)
rd(5)
shamt
func(6)
rs
rt
rd
bit21-25
bit16-20
bit11-15
Bnegate | op | function
0 | 00 | and
0 | 01 | Or
0 | 10 | Add
1 | 10 | Sub
1 | 11 | Slt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
control
32bits data
ALUC

## Slide 46: I type Instruction & Data stream
rs
rt
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
control
address
Write data
Read data
Sign extend
op(6)
rs(5)
rt(5)
Immediate data
bit0-15
bit21-25
bit16-20
MemWrite
MemRead
16
32
32bits data
lw $t0, 200($s2)
if $s2=1000，it will load word in element number 1200 to $t0
lw $t0, 200($s2)
Data
Memory
ALUC
ALUop

## Slide 47: I type Instruction & Data stream of beq
rs
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Sign extend
op(6)
rs(5)
rt(5)
offset
bit0-15
bit21-25
bit16-20
16
32
Shift
left 2
PC+4 from instructiondatapath
ADD
To PC
control
ALUC
Branch
ALUop

## Slide 48: J type Instruction
rs
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Sign extend
bit0-15
bit21-25
bit16-20
16
32
Shift
left 2
ADD
To PC
control
Branch
PC+4[31:28]##bit25-00##00
Jump
bit25-00
Shift left 2
##
28
PC+4[31:28]
bit25-00##00
J Loop
op(6)
Target address(26)

## Slide 49: Combine the datapath R & I type
rs
rt
rd
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
op(6)
rs(5)
rt(5)
Immediate data
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
MUX
MUX
bit11-15
MUX
ALU operation
Shift
left 2
MUX
ADD
To PC
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction

## Slide 50: Combine the datapath R & I type
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
MUX
MUX
bit11-15
MUX
ALU operation
Shift
left 2
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction

## Slide 51: Combine the datapath R & I type
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
MUX
MUX
bit11-15
MUX
ALU operation
Shift
left 2
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
R

## Slide 52: Combine the datapath R & I type
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
MUX
MUX
bit11-15
MUX
ALU operation
Shift
left 2
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
I-LW

## Slide 53: Combine the datapath R & I type
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
MUX
MUX
bit11-15
MUX
ALU operation
Shift
left 2
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
I-SW

## Slide 54: Combine the datapath R & I type
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Sign extend
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
MUX
MUX
bit11-15
MUX
ALU operation
Shift
left 2
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
I-beq

## Slide 55: Contents of Chapter 5
5.1 Introduction and Logic design Conventions
5.2 Building a datapath
5.3 A Simple Implementation Scheme
5.4 A Multicycle Implementation
5.5 Microprogramming
5.6 Exception

## Slide 56
Processor Design……
Controller Design
CTRL
Next CLK
Datapath
Memory

## Slide 57: Building the Datapath & Controller
Use multiplexors to stitch them together
  There are 7+3 signals
Note : Page 306 F5.16

## Slide 58: Building Controller
Analyse for cause and effect
Information comes from the 32 bits of the instruction
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
ALU's operation based on instruction type and function code
R-format instruction (add, sub, and, or, slt) |  |  |  |  | 
31 21 | 25 21 | 25 16 | 15 11 | 10 6 | 5 0
Op | Rs | Rt | Rd | Shamt | Funct
6 bits | 5bits | 5bits | 5bits | 5bits | 6bits
I-format instruction (lw, sw, beq) |  |  |  |  | 
Op | Rs | Rt | Immediate |  | 
6 bits | 5bits | 5bits | 16bits |  | 
J-format instruction (add, sub, and, or, slt) |  |  |  |  | 
Op | address |  |  |  | 
6 bits | 26bits |  |  |  | 

## Slide 59: Instruction Code: Input P103
Operations comes from the OPcode of the instruction
Instruction Code |  |  |  |  |  |  |  | 
 |  | 31 21 | 25 21 | 25 16 | 15 11 | 10 6 | 5 0 | 
add | R | 000000 | rs | rt | rd | 00000 | 100000 | 
sub | R | 000000 | rs | rt | rd | 00000 | 100010 | 
and | R | 000000 | rs | rt | rd | 00000 | 100100 | 
or | R | 000000 | rs | rt | rd | 00000 | 100101 | 
slt | R | 000000 | rs | rt | rd | 00000 | 101010 | 
lw | I | 100011 | rs | rt | Immediate(displacement) |  |  | 
sw | I | 101011 | rs | rt | Immediate(displacement) |  |  | 
beq | I | 000100 | rs | rt | Immediate(offset) |  |  | 
j | J | 000010 | address |  |  |  |  | 

## Slide 60: What should ALU do ?
e.g. what should the ALU do with these instructions
Example: lw $1, 100($2) OP rs rt 16 bit displacement
ALU control input
3 –types
(100011)35
2
1
100
(101011)43
2
1
100
000000(00)
rs(5)
rt(5)
rd(5)
shamt
func(6)
lw
sw
R
00
00
10
ALU op
B negate | op | function
0 | 00 | and
0 | 01 | Or
0 | 10 | Add
1 | 10 | Sub
1 | 11 | Slt
Why is the code for subtract 110
and not 011?

## Slide 61: Scheme of Controller
2-level decoder
First
Main
decoder
ALU
Decoder
Second
Signals for Other
Components
(7)
op(6)
rs(5)
rt(5)
rd(5)
shamt
func(6)
ALU operation(3)
ALU op(2)
instruction op code
(6)
Defined
Defined
Defined at Chapter-3

## Slide 62: The ALU control is where and other signals(7)
ALU OP
Output signals
ALU Control
Instroction[5:0]

## Slide 63: Signals for datapath Defined 7+2 control (p. 305)
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegDst | Select register destination number from the rt(20:16) when WR | Select register destination number from the rd(15:11) when WB
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScr | The second ALU operand come from the second register file output (Read data 2) | The second ALU operand is the sign-extended lower 16 bits of the instruction..
PCSrc (Branch) | The PC is replaced by the output of the adder that computers the value PC+4 | The PC is replaced by the output of the adder that computers the branch target.
MemRead | None | Data memory contents designated by the address input are put on the Read data output.
MemWrite | None | Data memory contents designated by the address input are replaced by value on the Write data input.
MemtoReg | The value fed to register Write data input comes from the Alu | The value fed to the register Write data input comes from the data memory.

## Slide 64: Our Simple Control Structure
All of the logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce right answer? right away
  we use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
Instruction n
Instruction n+1
控制器
时钟下触发下一条指令
Datapath
Memory
We are ignoring some details like setup and hold times

## Slide 65: Designing the Main Control Unit First level
Main Control Unit function
  ALU op (2)
  Divided 7 control signals into 2 groups
    4 Mux
    3 R/W
ALU
control
Instruction op code (6)
ALU op (2)
Mux (4)
R/W (3)
RegDst
ALUScr
PCSrc
MemtoReg
MemRead
MemWrite
RegWrite
LW | 00
SW | 00
Beq | 01
R-type | 10

## Slide 66: Truth Table for Main decoder
Instruction | RegDst | ALUSrc_B | MemtoReg | RegWrite | MemRead | MemWrite | Branch | ALUop1 | ALUop0
R-format |  |  |  |  |  |  |  |  | 
LW |  |  |  |  |  |  |  |  | 
SW |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
R-format | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
LW | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
SW | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0
beq | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 1

## Slide 67: Truth tables & Circuitry of main Controller
L/S 00
beq 01
R-type 10
输入 |  | 输出 |  |  |  |  |  |  |  |  | 
Instruction | OPCode | RegDst | ALUSrcB | Memto-Reg | Reg Write | Mem Read | Mem Write | Branch | Jump | ALUOp1 | ALU Op0
R-format | 000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
Lw(I-Type) | 100011 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0
sw(I-Type) | 101011 | X | 1 | X | 0 | 0 | 1 | 0 | 0 | 0 | 0
beq(I-Type) | 000100 | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 0 | 1
Jump | 000010 | X | X | X | 0 |  | 0 | 0 | 1 | X | X
Truth tables
Simple combinational logic

## Slide 68: Main Controller Code

## Slide 69: Designing the ALU decoder Second level
Must describe hardware to compute 3-bit ALU control input
Instruction opcode | ALUop | Instruction operation | Funct field | Desired ALU action | ALU control Input
LW | 00 | Load word | xxxxxx | Load word | 0010
SW | 00 | Store word | xxxxxx | Store word | 0010
Beq | 01 | branch equal | xxxxxx | branch equal | 0110
R-type | 10 | add | 100000 | add | 0010
R-type | 10 | subtract | 100010 | subtract | 0110
R-type | 10 | AND | 100100 | AND | 0000
R-type | 10 | OR | 100101 | OR | 0001
R-type | 10 | Set on less than | 101010 | Set on less than | 0111
 | 10 | NOR | 100111 | NOR | 0100

## Slide 70: Truth Table for ALU decoder
Describe it using a truth table (can turn into gates):
don’t care

## Slide 71: The ALU control signals -- logic circuit
0 | x | x | 1
0 | 0 | 1 | x
x | x | x | x
x | x | x | 1
F1F0
F3F2
F1
1 | x | x | 1
0 | 0 | 0 | X
x | x | x | X
1 | x | x | 1
F1F0
F3F2
F2
0 | x | x | 0
0 | 1 | 0 | X
x | x | x | X
x | x | x | 1
F1F0
F3F2
F0F1
F3

## Slide 72: ALU Controller Code

## Slide 73: The Datapath in operation for R-type
Address
Data
memory
Read
data
Write
data
Add
ALU
result
Shift
left 2
Shift
left 2
26
Instruction [25-0]
jump address[31-0]
28
PC+4[31-28]
Sign
extend
Instruction [15-0]
16
32
I-type |  |  | 
Op | rs | rt | Immediate
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Registers
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control
Control
Add
pc
4
Instruction [31-26]
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
1
M
U
X
0
jump
add sub and or slt

## Slide 74: The Datapath in operation for load
26
28
Instruction [15-11]
Write
data
Add
ALU
result
Shift
left 2
Read
register 2
Read
data 2
Instruction [20-16]
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Write
register
Write
data
Read
data 1
Registers
Address
Data
memory
Read
data
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
load instruction

## Slide 75: The Datapath in operation for store
Read
data
1
M
U
X
0
Write
register
Write
data
0
M
U
X
1
26
28
Instruction [15-11]
Add
ALU
result
Shift
left 2
Read
data 2
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Read
register 1
Read
data 1
Registers
Data
memory
0
M
U
X
1
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
store instruction
Read
register 2
Instruction [20-16]
Instruction
memory
Write
data
Address
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control

## Slide 76: The Datapath in operation for beq
Write
data
Address
ALU
result
Read
data
1
M
U
X
0
Write
register
Write
data
0
M
U
X
1
26
28
Instruction [15-11]
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Read
register 1
Read
data 1
Registers
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
beq instruction
Read
register 2
Instruction [20-16]
Instruction
memory
0
M
U
X
1
ALU
ALU
control
Add
ALU
result
Shift
left 2
0
M
U
X
1
Data
memory
Read
data 2
Zero

## Slide 77: j instruction
instruction format
  j Label
Implementation
  pc = pc28~31 ## 26bits-address × 4
000010/2
26 bits address

## Slide 78: The Datapath in operation for Jump
Registers
0
M
U
X
1
ALU
control
0
M
U
X
1
Read
data 2
Zero
Read
register 1
Read
data 1
Read
register 2
Add
ALU
result
Data
memory
Sign
extend
Instruction [25-21]
Instruction [15-0]
16
32
Instruction [20-16]
ALU
Shift
left 2
I-type |  |  | 
Op | rs | rt | Immediate
Write
data
Address
ALU
result
Read
data
0
M
U
X
1
Write
register
Write
data
0
M
U
X
1
Instruction [15-11]
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Control
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
1
M
U
X
0
jump
jump instruction
Instruction
memory
Jump-type | 
Op | address
28
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
Instruction [31-26]
26
Read
address
Instruction
[31-0]
Add
pc
4

## Slide 79: Single Cycle Implementation performance for lw
Calculate cycle time assuming negligible delays except:
  memory (2ns), ALU and adders (2ns), register file access (1ns)
2ns
2ns
2ns
1+1=2ns

## Slide 80: Performance in Single Cycle Implementation
Let’s see the following table:
Instruction class | Instruction memory | Register read | ALU | Data memory | Register write | Total
R-format | 2 | 1 | 2 |  | 1 | 6 ns
Load word | 2 | 1 | 2 | 2 | 1 | 8 ns
Store word | 2 | 1 | 2 | 2 |  | 7 ns
Branch | 2 | 1 | 2 |  |  | 5 ns
Jump | 2 |  |  |  |  | 2 ns
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.

## Slide 81: The CPU Performance Equation
CPU time=I CPI τ

## Slide 83
CPU performance is dependent upon three characteristics:
  clock cycle (or rate)
  clock cycles per instruction
  and instruction count.
It is difficult to change one parameter in complete isolation from others because the basic technologies involved in changing each characteristic are interdependent:
  Clock cycle time—Hardware technology and organization
  Clock cycle time—Hardware technology and organization
  Instruction count—Instruction set architecture and compiler technology

## Slide 84: MIPS (million instruction per second)
Three problems with MIPS:
    MIPS is dependent on the instruction set, making it difficult to compare MIPS of computers with different instruction sets.
  MIPS varies between programs on the same computer.
  Most importantly, MIPS can vary inversely to performance!
The bigger the MIPS, the faster the machine.

## Slide 85: Single Cycle Problems
what if we had a more complicated instruction like floating point?
  If so, the waste of time will be more serious.
wasteful of area. The reason is the following:
  Let’s see the instruction ‘mult’. This instruction needs to use the ALU repeatedly.
  But, in the single cycle implementation, one ALU can be used only once in one clock cycle.
  So, the instruction ‘mult’ will need many ALUs. The CPU will be very large.

## Slide 86: One Solution for Single Cycle Problems
One Solution:
  Use a smaller cycle time
  Let different instructions take different numbers of cycles
a Multicycle datapath:

## Slide 87
END