## Slide 1: Chapter 8
Storage Network and other I/O Topics

## Slide 2: Contents
8.1 Introduction
8.2 Disk Storage and Dependability
8.3 Networks (Skim)
8.4 Buses and Other Connections between Processors Memory, and I/O Devices
8.5 Interfacing I/O Devices to the Memory, Processor, and Operating System
8.6 I/O Performance Measures: Examples from Disk and File Systems
8.7 Designing an I/O system
8.8 Real Stuff: A Typical Desktop I/O System

## Slide 3
I/O Designers must consider many factors
  such as expandability and resilience(resume),as well as performance.
Assessing I/O system performance is very difficult.
  Different situations need different measurements.
Performance of I/O system depends on:
  connection between devices and the system
  the memory hierarchy
  the operating system
8.1 Introduction

## Slide 4
Typical collection of I/O devices

## Slide 5
Three characteristics
  Behavior
    Input (read once), output (write only, cannot read) ,or storage (can be reread and usually rewritten)
  Partner
    Either a human or a machine is at the other end of the I/O device, either feeding data on input or reading data on output.
  Data rate
    The peak rate at which data can be transferred between the I/O device and the main memory or processor.

## Slide 6
I/O performance depends on the application:
  throughput:
    In these cases, I/O bandwidth is the most important. Even I/O bandwidth can be measured in two different ways according to different situations:
      1.How much data can we move through the system in a certain time? For example, in many supercomputer applications, most I/O requires are for long streams of data, and transfer bandwidth is an important characteristic.

## Slide 7
      2.How many I/O operations can we do per unit of time?
      For example, National Income Tax Service mainly processes large number of small files.
  response time (e.g., workstation and PC)
  both throughput and response time (e.g., ATM)

## Slide 8
The diversity of I/O devices

## Slide 9
Important but neglected
  “The difficulties in assessing and designing I/O
  systems have often relegated I/O to second
  class status”
  “courses in every aspect of computing, from
  programming to computer architecture often
  ignore I/O or give it scanty coverage”
  “textbooks leave the subject to near the end,
  making it easier for students and instructors to
  skip it!”

## Slide 10
Amdahl’s law remind us that ignoring I/O is dangerous
  Assume:
    a bench mark executes in 100 seconds of elapsed time , where 90 seconds is for CPU and the rest is for I/O.
    CPU performance doubles per year, but I/O time doesn’t improve.
    How much faster will our program run after three years?
  Elapsed time = CPU time+ I/O time
  Improvement in CPU performance is 90/11 = 8 times
  Improvement in elapsed time is only 100/21= 4.5 times.

## Slide 11: 8.2 Disk Storage and Dependability
Two major types of magnetic disks
  floppy disks
  hard disks
    larger
    higher density
    higher data rate
    more than one platter

## Slide 12
The organization of hard disk
  platters: disk consists of a collection of platters, each of which has two recordable disk surfaces
  tracks: each disk surface is divided into concentric circles
  sectors: each track is in turn divided into sectors, which is the smallest unit that can be read or written

## Slide 13
Disks are organized into platters, tracks, and sectors

## Slide 14: What’s Inside A Disk Drive?

## Slide 15
To access data of disk(p562):
  Seek: position read/write head over the proper track
    minimum seek time
    maximum seek time
    average seek time (3 to 14 ms)
  Rotational latency: wait for desired sector
    average latency is the half-way round the disk.
Average rotational latency =
0.5
rotation
5400RPM
=
5400RPM
= 0.0056
seconds =
5.6 ms
0.5
rotation
/
60
seconds
minute
Average rotational latency =
0.5
rotation
15000RPM
=
15000RPM
= 0.0020
seconds =
2.0 ms
0.5
rotation
/
60
seconds
minute

## Slide 16
  Transfer: time to transfer a sector (1 KB/sector): function of rotation speed, Transfer rate of today’s drives - 30 to 80 MBytes/second
  Disk controller, which controls the transfer between
  the disk and the memory
＝6ms ＋
0.5
10,000PRM
＋
0.5KB
50MB/sec
＋ 0.2ms
＝6ms ＋ 3.0 ＋ 0.01 ＋ 0.2 ＝9.2ms
Access Time = Seek time + Rotational Latency + Transfer time + Controller Time
Disk Read Time 512B/sector
Assuming the measured seek time is 25% of the calculated average
Access Time ＝25%×6ms ＋ 3.0 ms＋ 0.01ms ＋ 0.2ms ＝4.7ms

## Slide 17: Dependability, Reliability, Availability
Computer system dependability is the quality of delivered service such that reliance can justifiably be placed on this service. The service delivered by a system is its observed actual behavior as perceived by other system (s) interacting with this system’s users.
Each module also has an ideal specified behavior, where a service specification is an agreed description of the expected behavior. A system failure occurs when the actual behavior deviates from the specified behavior. (p559)
Service accomplishment, where the service is delivered as specified
Service interruption, where the delivered service is different from the specified service

## Slide 18: Measure(p559)
MTTF mean time to failure 平均无故障时间
MTTR mean time to repaire 平均修复时间
MTBF (Mean Time Between Failures) 平均故障间隔时间 = MTTF+ MTTR
Availability
MTTF
MTTF+MTTR
Availability=

## Slide 19: Three way to improve MTTF
Fault avoidance:
  preventing fault occurrence by construction
  Fault tolerance:
  using redundancy to allow the service to comply with the service specification despite faults occurring, which applies primarily to hardware faults
  Fault forecasting:
  predicting the presence and creation of faults, which applies to hardware and software faults

## Slide 20: RAID: Redundant Arrays of Inexpensive Disks
A disk arrays replace larger disk
Error Checking and Correcting

## Slide 21: Use Arrays of Small Disks?
Low End
High End
3.5”
Disk Array: 1 disk design
14”
10”
5.25”
3.5”
Conventional: 4 disk designs
Katz and Patterson asked in 1987:
  Can smaller disks be used to close gap in performance between disks and CPUs?

## Slide 22: Array Reliability
Reliability of N disks = Reliability of 1 Disk ÷ N
  50,000 Hours ÷ 70 disks = 700 hours
Disk system MTTF: Drops from 6 years to 1 month!
• Arrays (without redundancy) too unreliable to be useful!
Hot spares support reconstruction in parallel with access: very high media availability can be achieved

## Slide 23: Redundant Arrays of (Inexpensive) Disks
Files are "striped" across multiple disks
Redundancy yields high data availability
  Availability: service still provided to user, even if some components failed
Disks will still fail
Contents reconstructed from data redundantly stored in the array
   Capacity penalty to store redundant info
   Bandwidth penalty to update redundant info

## Slide 24: RAID 0: No Redundancy(p587)
• Data is striped across a disk array but there is no redundancy to tolerate disk failure.
It also improves performance for large accesses,
since many disks can operate at once.
RAID 0 is something of a misnomer as there is no Redundancy,(p587)
Notes: Misnomer: 使用不当的名称

## Slide 25: RAID 1: Disk Mirroring/Shadowing
• Each disk is fully duplicated onto its “mirror”
Very high availability can be achieved
• Bandwidth sacrifice on write:
Logical write = two physical writes
  • Reads may be optimized
• Most expensive solution: 100% capacity overhead
(RAID 2 not interesting, so skip)
recovery
group

## Slide 26: RAID 3: Bit-Interleaved Parity Disk
P
10010011
11001101
10010011
. . .
logical record
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
P contains sum of
other disks per stripe mod 2 (“parity”)
If disk fails, subtract
P from sum of other disks to find missing information
Striped physical
records

## Slide 27: Inspiration for RAID 4
RAID 3 relies on parity disk to discover errors on Read
Every sector has an error detection field
Relies on error detection field to catch errors on read, not on the parity disk
Allows independent reads to different disks simultaneously

## Slide 28: RAID 4: High I/O Rate Parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Address
Stripe
Insides of 5 disks
Example:
small read D0 & D5, large write D12-D15

## Slide 29: Problems of Disk Arrays: Small Writes
RAID-4: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes

## Slide 30: Inspiration for RAID 5
RAID 4 works well for small reads
Small writes (write to one disk):
  Option 1: read other data disks, create new sum and write to Parity Disk
  Option 2: since P has old sum, compare old data to new data, add the difference to P
Small writes are limited by Parity Disk: Both Writes to D0 and D5 also write to P disk
D0
D1
D2
D3
P
D4
D5
D6
P
D7

## Slide 31: RAID 5: High I/O Rate Interleaved Parity
Independent writes are
possible because of
interleaved parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Example: write to D0, D5 uses disks 0, 1, 3, 4

## Slide 32: RAID 6: P+Q Redundancy
When a single failure correction is not sufficient, Parity can be generalized to have a second calculation over data and another check disk of information.

## Slide 33: RAID Techniques: Goal is performance, popularity due to reliability of storage
• Disk Mirroring, Shadowing (RAID 1)
Each disk is fully duplicated onto its "shadow"
Logical write = two physical writes
100% capacity overhead
• Parity Data Bandwidth Array (RAID 3)
Parity computed horizontally
Logically a single high data bw disk
• High I/O Rate Parity Array (RAID 5)
Interleaved parity blocks
Independent reads and writes
Logical write = 2 reads + 2 writes
1
0
0
1
0
0
1
1
1
1
0
0
1
1
0
1
1
0
0
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
0
1
0
0
1
1
1
0
0
1
0
0
1
1

## Slide 34
8.3 Networks (skim)
  Key characteristics of typical networks include
  the following
    Distance: 0.01 to 10,000 kilometers
    Speed: 0.001MB/sec to 100MB/sec
    Topology: Bus, ring, star, tree
    Shared lines: None (point-to-point) or shared (multidrop)

## Slide 35
  Local area network (LAN) e.g., Ethernet
  Packet-switched network ,which are common in long-haul networks
  e.g., ARPANET
  TCP/IP is the key to interconnecting different networks
  The bandwidths of networks are probably growing faster than the bandwidth of any other type of device at present.

## Slide 36: 8.4 Buses and Other Connections between Processors Memory, and I/O Devices(p568)
Shared communication link (one or more wires)
Difficult design:
  may be bottleneck
  length of the bus
  number of devices
  tradeoffs (fast bus accesses and high bandwidth)
  support for many different devices
  cost

## Slide 37
A bus contains two types of lines
  Control lines, which are used to signal requests and
  acknowledgments, and to indicate what types of
  information is on the data lines.
  Data lines, which carry information (e.g., data, addresses, and
  complex commands) between the source and the destination.
Bus transaction
  include two parts: sending the address and receiving or
  sending the data
  two operations
    input: inputting data from the device to memory
    output: outputting data to a device from memory

## Slide 38
The steps of an output operation.
Initial a read from memory. Control lines signal a read request to memory, while the data lines contain the address
Memory access the data.
Memory transfers data and signal data is available. The device stores data as it appears on the bus.

## Slide 39
The steps of an input operation.
Control lines indicate a write request for memory, while the data lines contain the address
When the memory is ready, it signals the device, which then transfers the data. The memory will store the data as it receives it . The device need not wait for the store to be completed.

## Slide 40
Types of buses: (p566)
  processor-memory (short, high speed, custom design)
  backplane (high speed, often standardized, e.g., PCI)
  I/O (lengthy, different devices, standardized, e.g., SCSI)
Older PCs often use a single bus for processor-to-memory communication, as well as communication between I/O devices and memory.

## Slide 41
A separate bus is used for processor-memory traffic. The I/O bus use a bus adapter to interface to the processor-memory bus.
A separate bus is used for processor-memory traffic. A small number of backplane buses tap into the processor-memory bus.

## Slide 42
Synchronous vs. Asynchronous
  Synchronous bus use a clock and a synchronous protocol,
  fast and small but every device must operate at same rate
  and clock skew requires the bus to be short
  Asynchronous bus don’t use a clock and instead use
  handshaking
  Our example ,which illustrates how asynchronous buses
  use handshaking, assumes there are three control lines.
    ReadReq: Used to indicate a read request for memory. The address is
    put on the data lines at the same time.
    DataRdy: Used to indicate that data word is now ready on the data lines.
    Ack: Used to acknowledge the ReadReq or the DataRdy signal of the
    other party
Handshaking protocol

## Slide 43
Example: The asynchronous handshaking consists of seven steps to read a word from memory and receive it in an I/O device.
When memory saw the ReadReq line, it reads the address from the data bus, starts the memory read operation，then raises Ack to tell the device that the ReadReq signal has been seen.
I/O device saw the Ack line high and releases the ReadReq data lines.
3. Memory sees that ReadReq is low and drops the Ack line.

## Slide 44
When the memory has the data ready, it places the data on the data lines and raises DataRdy.
5. The I/O device sees DataRdy, reads the data from the bus , and signals that it has the data by raising ACK.
The memory sees Ack signals, drops DataRdy, and releases the data lines.
7. Finally, the I/O device, seeing DataRdy go low, drops the ACK line, which indicates that the transmission is completed.
Example: The asynchronous handshaking consists of seven steps to read a word from memory and receive it in an I/O device.

## Slide 45
These finite state machines implement the control for handshaking protocol illustrated in former example.

## Slide 46
Obtaining Access to the Bus
  “Without any control, multiple device desiring to
  communicate could each try to assert the control and
  data lines for different transfers!”
  So,a bus master is needed. Bus masters initiate and control all bus requests.
  e.g., processor is always a bus master.
  Example: the initial steps in a bus transaction with a
  single master (the processor).
First, the device generates a bus request to indicate to the processor that it wants to use the bus.

## Slide 47
The processor responds and generates appropriate bus control signals. For example, if the devices wants to perform output from memory, the processor asserts the read request lines to memory.
The processor also notifies the device that its bus request is being processed; as a result, the device knows it can use the bus and places the address for the request on the bus.

## Slide 48: Bus Arbitration
一般都是多个设备共享一条总线进行数据通信，其中如果多个设备同时发送接收数据的话，从而产生总线竞争，会导致通信冲突导致通信失败，所以在总线上要引入一个仲裁机制来决定什么时间谁来占用总线的通信

## Slide 49
Bus Arbitration
  Deciding which bus master gets to use the bus next
  In a bus arbitration scheme, a device wanting to use the
  bus signals a bus request and is later granted the bus.
  four bus arbitration schemes:
    daisy chain arbitration (not very fair):菊花链，阻塞式级联
    centralized, parallel arbitration (requires an arbiter), e.g., PCI
    self selection, e.g., NuBus used in Macintosh
    collision detection, e.g., Ethernet
Two factors in choosing which device to grant the bus:
  bus priority
  fairness
Notes: (1) 链式查询方式
链式查询方式的主要特点：总线授权信号BG串行地从一个I/O接口传送到下一个I/O接口。假如BG到达的接口无总线请求，则继续往下查询；假如BG到达的接口有总线请求，BG信号便不再往下查询，该I/O接口获得了总线控制权。离中央仲裁器最近的设备具有最高优先级，通过接口的优先级排队电路来实现。
链式查询方式的优点: 只用很少几根线就能按一定优先次序实现总线仲裁，很容易扩充设备。
链式查询方式的缺点: 对询问链的电路故障很敏感，如果第i个设备的接口中有关链的电路有故障，那么第i个以后的设备都不能进行工作。查询链的优先级是固定的，如果优先级高的设备出现频繁的请求时，优先级较低的设备可能长期不能使用总线。
(2) 集中仲裁：用在高速设备上，由优先算法或者策略决定谁可以使用总线
（4）碰撞检测：比较公平的一种方式。就是计算机边发送数据边检测信道上的信号电压大小。当一个站检测到的信号电压摆动值超过一定的门限值时，就认为总线上至少有两个站同时在发送数据，表明产生了碰撞。在发生碰撞的时候，总线上传输信号产生了严重的失真，无法从中恢复出有用的信息来。每一个正在发送数据的站，一旦发现总线上产生了碰撞，就立即停止发送，以免继续浪费资源，再等待一段时间后再次发送。
发送数据的站一旦发现发生碰撞时，除了立即停止发送数据外，还要继续发送若干比特的认为干扰信号，以便让所有用户都知道已经发生了碰撞。

## Slide 50
Bus Standards
  SCSI (small computer system interface)
  PCI (peripheral component interconnect)
  IPI (intelligent peripheral interface)
  IBMPC-AT IBMPC-XT
  ISA EISA
Notes: ISA速度慢，EISA快，都用的比较少了
PC总线－－标准的总线IBMPC/-XT 20位地址线，8位数据线； IBMPC-AT总线，EISA 16位；

## Slide 51: The Buses and Networks of Pentium(p571)
Processor
FSB
(G)MCH
Analog
Display
VGA
AGP or
PCI Exp.
Graphics
Card
System
Memory
ICH
DMI/Hub Interface
IDE (& SATA))
USB
GPIO
Power Management
Clock Generation
LAN
System Management
SMBus/I2C
Other ASIC
(Optional)
Super IO
BIOS Support
/ Firmware Hub
Low Pin Count
(LPC) Interfaces
Key Board
Mouse
…
PCI Bus
G_Ethernet
PCI Exp.
AC’97 Codecs

## Slide 52: 8.5 Interfacing I/O Devices to the Memory, Processor, and Operating System(p572)
Three characteristics of I/O systems
  shared by multiple programs using the processor.
  often use interrupts to communicate information about I/O operations.
  The low-level control of I/O devices is complex
Three types of communication are required:
  The OS must be able to give commands to the I/O devices.
  The device must be able to notify the OS, when I/O device completed an operation or has encountered an error.
  Data must be transferred between memory and an I/O device

## Slide 53
  Giving Commands to I/O Devices
  Two methods used to address the device
  memory-mapped I/O:
    portions of the memory address space are assigned to I/O devices,and lw and sw instructions can be used to access the I/O port.
  special I/O instructions
    Give a command to an I/O device
  command port ,data port
    The Status register (a done bit, an error bit……)
    The Data register, The command register

## Slide 54
  Communication with the Processor
  I/O SYTEM DATA TRANSFER CONTROL MODE
  Polling: The processor periodically checks status bit to see if it is time for the next I/O operation.
  Interrupt: When an I/O device wants to notify processor that it has completed some operation or needs attentions, it causes processor to be interrupted.
  DMA (direct memory access): the device controller transfer data directly to or from memory without involving processor.

## Slide 55: Interrupt-Driven I/O mode
t
t
CPU
Printer
Idle
Ready
start
Request
interrupt
Incept Data
Printing
Request
interrupt
Incept Data
Printing
start
I/O
Response
interrupt
Transfer
Data
Response
interrupt
Transfer
Data
Interrupt return
return
Service for interruption
Service for interruption
Running
main program
go on doing
main program
main program
Advantage: concurrent operation

## Slide 56: DMA transfer mode
CPU
memory
I/O DEVICE
DMA
CPU INITIATION DMA
NO DMA I/O-CPU--M
DMA-- I/O---M I/O DIRECT ACCESS MEMORY

## Slide 57
A DMA transfer need three steps:
  The processor sets up the DMA by supplying some
  information, including the identity of the device, the
  operation, the memory address that is the source or
  destination of the data to be transferred, and the number
  of bytes to transfer.
  The DMA starts the operation on the device and arbitrates
  for the bus. If the request requires more than one transfer
  on the bus, the DMA unit generates the next memory
  address and initiates the next transfer.
  Once the DMA transfer is complete, the controller
  interrupts the processor, which then examines whether
  errors occur.

## Slide 58
Compare polling, interrupts, DMA
  The disadvantage of polling: wasting processor time. When the CPU polls the I/O devices periodically, the I/O devices maybe have no request or have not get ready.
  If the I/O operations is interrupt driven, the OS can work
  on other tasks while data is being read from or written to
  the device.
  Because DMA doesn’t need the control of processor, it
  will not consume much of processor time.

## Slide 59: 8.6 I/O Performance Measures: Examples from Disk and File Systems
Supercomputer I/O Benchmarks
Transaction Processing I/O Benchmarks
  I/O rate: the number of disk access per second, as opposed to data rate.
File System I/O Benchmarks
  MakeDir, Copy, ScanDir, ReadAll, Make

## Slide 60
Performance analysis of Synchronous versus
Asynchronous buses
Assume: The synchronous bus has a clock cycle time of 50 ns, and each
bus transmission takes 1 clock cycle .
The asynchronous bus requires 40 ns per handshake.
The data portion of both buses is 32 bits wide.
Question: Find the bandwidth for each bus when reading one word from a 200-ns memory.
  synchronous bus:
  the bus cycles is 50 ns. The steps and times required for the
  synchronous bus are follows:
  1. Send the address to memory : 50ns
  2. Read the memory : 200ns
  3. Send the data to the device : 50ns
  Thus, the total time is 300 ns. So,
  the bandwidth = 4bytes/300ns = 4MB/0.3seconds
  = 13.3MB/second
Answer:

## Slide 61
  asynchronous bus:
  If we look carefully at the right Figure, we realize that several of the steps can be overlapped with the memory access time.
  In particular, the memory receives the address at the end of step 1 and does not need to put the data on the bus until the beginning of step 5; steps 2, 3, and 4 can overlap with the memory access time.
  This leads to the following timing:
  step1: 40ns
  step2,3,4: maximum(3×40ns,200ns)=200ns
  step5,6,7: 3×40ns=120ns
  Thus, the total time is 360ns, so
  the maximum bandwidth = 4bytes/360ns = 4MB/0.36seconds
  =11.1MB/second
  Accordingly, the synchronous bus is only about 20% faster. (Why?)

## Slide 62
Suppose we have a system with the following characteristic:
1. A memory and bus system supporting block access of 4 to 16 32-bit words
2. A 64-bit synchronous bus clocked at 200 MHz, with each 64-bit transfer taking 1 clock cycle, and 1 clock cycle required to send an address to memory.
3. Two clock cycles needed between each bus operation.
4. A memory access time for the first four words of 200ns; each additional set of four words can be read in 20 ns. Assume that a bus transfer of the most recently read data and a read of the next four words can be overlapped.
Find the sustained bandwidth and the latency for a read of 256 words for transfers that use 4-word blocks and for transfers that use 16-word blocks. Also compute effective number of bus transactions per second for each case.
Increasing the Bus Bandwidth
  Increasing data bus width
  Use separate address and data lines
  transfer multiple words
Performance Analysis of Two Synchronous Bus Schemes.

## Slide 63
  The 4-word block transfers:
  each block takes
  1. 1 clock cycle to send the address to memory
  2. 200ns/(5ns/cycle) = 40 clock cycles to read memory
  3. 2 clock cycles to send the data from the memory
  4. Two clock cycles needed between each bus operation.
  This is a total of 45cycles.
  There are 256/4 = 64 blocks.
  So the transfer of 256 words takes
  45×64=2880 clock cycles
  The latency for the transfer of 256 words is:
  2880 cycles× 5ns/cycle = 14,400ns.
Answer:
64-bit synchronous bus

## Slide 64
The bus bandwidth is:
(256
×
4)bytes
×
1second
14,
400
ns
＝
71.11 MB/sec
so the number of bus transactions per second is:

## Slide 65
  the 16-word block transfers:
  the first block requires
  1. 1 clock cycle to send an address to memory
  2. 200ns or 40 cycles to read the first four words in memory.
  3. 2 cycles to transfer the data of the set, during which time the read of the next 4-word set is started.
  4. It only takes 20ns or 4 cycles to read the next set. After the read is completed, the set will be transferred. Each of the three remaining sets requires repeating only the last two steps.
  5. Two clock cycles needed between each bus operation.

## Slide 66
  Thus, the total number of cycles for each 16- word block is:
  1+40+4×3+2+2=57 cycles.
  There are 256/16=16 blocks.
  so the transfer of 256 words takes 57×16=912 cycles.
  Thus the latency is:
  912cycles× 5ns/cycles = 4560ns.
1
40
4(20ns)
4(next)
4(next)
send
interval
interval

## Slide 67
The number of bus transactions per second with 16-word blocks is:
The bus bandwidth with 16-word blocks is:
Now,let’s put two bus bandwidth together:
4-word blocks: 71.11 MB/sec
16-word blocks:224.56 MB/sec
The bandwidth for the 16-word blocks is 3.16 times higher than for the 4-word blocks.
(256
×
4)bytes
×
1second
4560
ns
＝
224.56 MB/sec

## Slide 68
**Overhead of Polling in an I/O System
Assume: that the number of clock cycles for a polling operation is 400 and that processor executes with a 500-Mhz clock.
Determine the fraction of CPU time consumed for the mouse, floppy disk, and hard disk.
We assuming that you poll often enough so that no data is ever lost and that those devices are potentially always busy.
We assume again that:
1. The mouse must be polled 30 times per second to ensure that we do not miss any movement made by the user.
2. The floppy disk transfers data to the processor in 16-bit units and has a data rate of 50 KB/sec. No data transfer can be missed.
3. The hard disk transfers data in four-word chunks and can transfer at 4 MB/sec. Again, no transfer can be missed.

## Slide 69
  the mouse:
  clock cycles per second for polling : 30×400=12,000 cycles
  Fraction of the processor clock cycles consumed is
Answer:
  the floppy disk:
  the number of polling access per second:
  50KB/2B = 25K
  clock cycles per second for polling: 25K×400cycles
  Fraction of the processor clock cycles consumed:

## Slide 70
  The hard disk:
  The number of polling access per second :
  4MB/16B = 250K
  Clock cycles per second for polling = 250K×400
  Fraction of the processor clock cycles consumed:
Clearly, polling can be used for the mouse without much performance impact on the processor, but it is unacceptable for a hard disk on this machine.
Now, let’s put three fractions together:
Mouse: 0.002%
Floppy disk: 2%
Hard disk: 20%

## Slide 71
Overhead of Interrupt-Driven I/O
Suppose we have the same hard disk and processor we used in the former example, but we used interrupt-driven I/O. The overhead for each transfer, including the interrupt, is 500 clock cycles. Find the fraction of the processor consumed if the hard disk is only transferring data 5% of the time.
Answer: First, we assume the disk is transferring data 100% of the time. So, the interrupt rate is the same as the polling rate.
  Cycles per second for disk is:
250K×500=125×106cycles per second
Fraction of the processor consumed during a transfer is:

## Slide 72
Now,we assume that the disk is only transferring data 5% of the time.The fraction of the processor time consumed on average is:
25%×5%=1.25%
As we can see, no CPU time is needed when an interrupt-driven I/O device is not actually transferring. This is the major advantage of an interrupt-driven interface versus polling.

## Slide 73
Overhead of I/O Using DMA
Suppose we have the same hard disk and processor we used in the former example.
  Assume that the initial setup of a DMA transfer takes 1000 clock cycles for the processor, and assume the handling of the interrupt at DMA completion requires 500 clock cycles for the processor.
  The hard disk has a transfer rate of 4MB/sec and uses DMA. The average transfer from disk is 8 KB. Assume the disk is actively transferring 100% of the time.
  Please find what fraction of the processor time is consumed.

## Slide 74: Answer: Time for each 8KB transfer is: 8KB/(4MB/second)=2×10-3seconds. It requires the following cycles per second:
Fraction of processor time:
Unlike either polling or interrupt-driven I/O, DMA can be used to interface a hard disk without consuming all the processor cycles for a single I/O.

## Slide 75: 8.7 Designing an I/O system
The general approaches to designing I/O system
  Find the weakest link in the I/O system, which is the component in the I/O path that will constrain the design. Both the workload and configuration limits may dictate where the weakest link is located.
  Configure this component to sustain the required bandwidth.
  Determine the requirements for the rest of the system and configure them to support this bandwidth.

## Slide 76
I/O System Design
Examples:
Consider the following computer system:
  1. A CPU sustains 3 billion instructions per second and it takes average 100,000 instructions in the operating system per I/O operation.
  2. A memory backplane bus is capable of sustaining a transfer rate of 1000 MB/sec.
  3. SCSI-Ultra320 controllers with a transfer rate of 320 MB/sec and accommodating up to 7 disks.
  4. Disk drives with a read/write bandwidth of 75 MB/sec and an average seek plus rotational latency of 6 ms.

## Slide 77
If the workload consists of 64-KB reads (assuming the data block is sequential on a track), and the user program need 200,000 instructions per I/O operation, please find the maximum sustainable I/O rate and the number of disks and SCSI controllers required.
The two fixed component of the system are the memory bus and the CPU. Let’s first find the I/O rate that these two components can sustain and determine which of these is the bottleneck.
Answer:

## Slide 78
The CPU is the bottleneck, so we can now configure the rest of the system to perform at the level dictated by the bus, 10000 I/Os per second.
Maximum I/O rate of CPU =
Instruction execution rate
Instruction per I/O
=
3
×
10
9
(200
＋
100)
×
10
3
＝
10000
I/Os
seconds
Maximum I/O rate of bus =
Bus bandwidth
Bytes per I/O
=
1000
×
10
6
64
×
10
3
= 15625
I/Os
seconds

## Slide 79
Now, let’s determine how many disks we need to be able to Accommodate 10000 I/Os per second. To find the number of disks, we first find the time per I/O operation at the disk:
This means each disk can complete 1000ms/6.9ms, or 146 I/Os per second. To saturate the bus, the system need 10000/146≈69 disks.
Time per I/O at disk =
Seek/rotational time + Transfer time
= 6 ms
＋
64KB
75MB/sec
= 6.9 ms

## Slide 80
To compute the number of SCSI buses, we need to know the average transfer rate per disk, which is given by:
Assuming the disk accesses are not clustered so that we can use all the bus bandwidth, we can place 7 disks per bus and controller. This means we will need 69/7, or 10 SCSI buses and controllers.
Transfer rate =
Transfer size
Transfer time
=
64KB
6.9ms
≈ 9.56MB/sec
7 × 9.56MB/sec<320MB/s
69 ÷ 7 ≈ 10